## Slide 1: Space Division Multiplexing combined with OFDM
REFAT KHAN

## Slide 2: Table of Contents
Broadband Wireless Communication Systems
Impact of Receiver diversity techniques
Some Diversity techniques
    Frequency and Time diversity
    Space diversity
    Polarization diversity
    Selection diversity
    Maximal Ratio and Equal Gain Combining
Multi-Antenna Link: Signal model and SDM techniques
Signal model

## Slide 3: Broadband Wireless Communication Systems
One example of a broadband wireless communication system is a wireless computer
network. Wireless computer networks are in demand in offices and universities.
Another example of a broadband wireless communication system is a wireless
communication system that uses Space Division Multiplexing (SDM). SDM is a technique
that transmits different data streams on different transmit antennas simultaneously.
This thesis will compare a number of SDM algorithms and combine the best algorithm
with Orthogonal Frequency Division Multiplexing (OFDM) to avoid Inter Symbol
Interference (ISI).

## Slide 4: Impact of Receiver diversity techniques
Before SDM techniques were developed, receiver diversity was seen as a powerful communication receiver technique that provided wireless link improvement at relatively low cost.
Diversity techniques try to solve the problem that transmission errors occur when the transmission channel attenuation is large, i.e., when the channel is in a deep fade.

## Slide 5: Frequency and Time diversity
Frequency diversity is a technique that improves the performance of wireless systems by transmitting the same signal on multiple frequencies. The receiver then selects the frequency that has suffered least from fading or combines the signals from all frequencies to improve the estimation of the transmitted signal.
Time diversity transmits the same signal multiple times, with a time spacing between transmissions that is greater than the coherence time of the channel. This ensures that the multiple repetitions of the signal will be received with independent fading conditions.

## Slide 6: Space diversity
Space diversity, also known as antenna diversity, is a technique that improves the performance of wireless systems by using multiple antennas. The antennas are separated by a distance of half a radio wavelength or more, which ensures that the signals received by the antennas are uncorrelated. This means that if one antenna receives a weak signal, another antenna is likely to receive a strong signal.

## Slide 7: Polarization diversity
In wireless communication, polarization diversity is used to enhance reliability. It involves transmitting the same signal on two antennas with different polarizations, exploiting uncorrelated paths and combining horizontally and vertically polarized signals at the receiver for improved quality. This provides two diversity branches, simplifies antenna placement, but mixing with other diversity methods may degrade performance. The choice of diversity technique depends on the specific communication environment and system requirements.

## Slide 8: Selection diversity
Selection Diversity The highest instantaneous SNR branch is connected to the demodulator.

## Slide 9: Maximal Ratio and Equal Gain Combining
Maximal Ratio combining : Maximum Ratio Combining (MRC) is an optimization technique for combining signals that are carrying the same information.
Equal Gain combining : An Equal Gain Combiner is obtained when the gains used in MRC are all set to unity. The disadvantage is that (like MRC) an individual receiver for each antenna element is needed. However, the possibility of producing an acceptable signal from a number of unacceptable inputs is still retained, and the performance is only marginally inferior to MRC and usually superior to selection diversity.

## Slide 10: Multi-Antenna Link: Signal model and SDM techniques
One way to increase the capacity of wireless communication systems is by exploiting the spatial dimension using multiple antennas at the receiver as well as at the transmitter. This type of transmission is called Space Division Multiplexing (SDM).
In this chapter, a number of different decoding algorithms for SDM will be discussed and their performance will be compared.

## Slide 11: Signal model
We consider a communication system comprising Nt transmit (TX) and Nr receive (RX) antennas that operates in a Rayleigh flat-fading environment and exploits the spatial dimension by using Space Division Multiplexing (SDM).
A channel is said to be a Rayleigh fading channel when the channel impulse response is modelled as a zero-mean complex-valued gaussian process .
In this case, the envelope of the channel impulse response at any time instant has a Rayleigh probability distribution and the phase is uniformly distributed in the interval (0,2p).
This can be shown as follows. Suppose we model the channel impulse response H as a zero-mean complex gaussian variable, like:
H = A + jB

## Slide 12: Signal model
Where A and B are zero-mean statistically independent real guassian variables, each having a variance s2/2. The variance of the complex gaussian variable H can be shown to be:
var(H ) = E[H 2 ]- E[H ]2 = E[(A + jB)(A + jB)] = E[A2 + 2 jAB + B 2 ]= E[A2 ]+ E[B 2 ]= s 2
We introduce a new variable
Y = A2 + B 2
Here Y is chi-squared Random variable

## Slide 13: Signal model
Hence, the probability density function (pdf) of Y is:
pY (y) = e - y / 2 , y 0
Now, suppose we define a random variable R to denote the envelope of the channel impulse response:
R = =
In order to find the pdf of R, we need to make a change of variables in the Probability Distribution Function
(PDF) of Y to first find the PDF of R:
FR(r) = P(R ≤ r) = P(Y ≤ r) = P( ≤ r²) = F(r²)

## Slide 14: Signal model
where the fact is used that r ³ 0. Then the pdf of R is given by
pR® = FR(r) = Fy(r2) = 2 r pY(r2) = e – r 2 / 2 , r 0
This is the pdf of a Rayleigh-distributed random variable; thus, the envelope of H has a Rayleigh probability distribution. The fact that the phase of H is uniformly distributed in the interval (0,2p) .
Suppose that at discrete times, the transmitter sends an Nt-dimensional (complex) signal vector s (i.e., it transmits Nt parallel streams of data), and the receiver records an Nr-dimensional complex vector x. Then the following signal model describes the relation between s and x:
x = Hs + ν
where H is an Nr ´ Nt complex propagation matrix ) and the vector ν (Nr- dimensional) represents additive receiver noise

## Slide 15: Signal model
The vector s is assumed to have zero-mean, uncorrelated random variables with variance equal to ss2. The vector s is assumed to have zero-mean, uncorrelated random variables with variance equal to ss2. The total power of s (i.e., E[s*s]) is assumed to be P. Thus, the covariance matrix of s equals:
E[s*s] = ss2 INt = INt
Where * denotes the conjugate transpose of a vector or matrix and the matrix I with subscript Nt represents the identity matrix with dimension Nt
The channel matrix is denoted by H. It is assumed the channel matrix H has independently and identically distributed (i.i.d.), zero-mean, complex Gaussian, unit variance entries (the variance of each entry is sc2 = 1). In other words, each component has a Rayleigh distribution (like H) with s2 = sc2 = 1. Thus, the system operates in a Rayleigh flat-fading environment.

## Slide 16: Signal model
The vector ν is Nr-dimensional and represents additive receiver noise. The vector ν is assumed to have zero-mean, uncorrelated random variables with variance sn2 and a covariance matrix equal to:
E[v*v] = sv2 INt
Furthermore, it is assumed that the vectors s and ν are independent and thus the following holds: E[sν* ] = 0 . With the above-described assumptions about the power of the signal and the noise, the expected Signal-to- Noise Ratio (SNR) per receiving antenna, i.e., the SNR for each component of x, can be found and is equal to
= = =
Where Es stands for the signal power per receive antenna and N0 denotes the noise power per receive antenna.

## Slide 17: Signal model
In order to explain the different Space Division Multiplexing techniques, the following notations will be used
where xi and si represent the i-th element of x and s respectively. Hi and hi denote the i-th row and i-th column of H, respectively.
In the following sections, a number of SDM decoding techniques for the receiver will be discussed and compared.

## Slide 18: The Zero Forcing Algorithm
Zero Forcing Algorithm in Adaptive Antenna Array (AAA):
  Zero Forcing algorithm is based on a conventional adaptive antenna array (AAA) technique.
  Known as linear combinatorial nulling
  Each sub stream is the desired signal.
  The remaining data streams are considered as "interferers“.
  Nulling of the "interferers" can be performed by choosing weight vectors di (with i =1,2, ..., Nt) such that
  Where T stands for transpose of a matrix.
  And stands for j-th column of the channel matrix H.

## Slide 19: The Zero Forcing Algorithm
Zero Forcing Algorithm in Adaptive Antenna Array (AAA):
  Solving the weight vectors is equal to finding a matrix D such that :
  D * H = I
  Where D is a matrix that represents the linear processing in the receiver.
  Forcing the ‘’interference’’ to zero , S is estimated
  If H is not square, then D equals the pseudo-inverse of H:
  D = H+ = (H*H)-1 H*
  Where + represent the pseudoinverse.
  Some constraint for Pseudo-inverse
    Nt Nr
    The column of H must be independent

## Slide 20: The Zero Forcing Algorithm
Zero Forcing Algorithm in Adaptive Antenna Array (AAA):
  If the inverse is the exists, the estimates of S can be found by:
    Sest = Dx
    = (H*H)-1 H* x
    Or equivalently:
    Sest = H+ x
  And for i-th Sest can be written as :
  (Sest)i = Hi+ x
  Hi+ represent the i-th row of H+ , is equal to the transpose of the i-th weight vector di
  di is the so-called nulling vector.

## Slide 21: The Zero Forcing Algorithm
Zero Forcing Algorithm in Adaptive Antenna Array (AAA):
  The ZF algorithm's performance can be tested through simulations, and its behavior can be theoretically understood by comparing it with the MRC system.
  Understanding the diversity order helps relate the ZF algorithm to the MRC system.
  This comparison gives valuable insights into the ZF algorithm's performance, making it crucial for evaluating wireless systems.

## Slide 22: Theoretical BER
System Operation and Decision Variable in Raleigh Flat-Fading Environment for BPSK:
  In a system operating under Raleigh flat-fading, the channel elements can be expressed for an MRC system with one transmit and L receive antennas
  The channel characteristics in the MRC system are determined by the channel elements , channel attenuation factor , and phase shift , assuming perfect channel knowledge.
  The system output in a Raleigh flat-fading environment is represented by a single decision variable U for BPSK with Lth-order diversity:
  U = Re ( xk ) = Re ( s + vk )
  Where vk denotes the complex gaussian noise and s is the transmitted symbol.

## Slide 23: Theoretical BER
Probability and SNR Analysis for BPSK in Flat-Fading Channels:
  For BSPK, The decision variable U is used in the decoder to recover the transmitted s.
  If U> 0 then s = and U < 0 then s = -
  For a fixed set of {} and the assumption that s = is transmitted.
  The Gaussian decision variable U, with mean noise power N0 per receive antenna, determines the probability of being less than zero is :
  P2 (b) = Q() where Q is the function as : Q(x) = dt and x

## Slide 24: Theoretical BER
BER Analysis and Error Rate Behavior with L-th Order Diversity in Flat-Fading Channels:
  The SNR per bit , b is given as :
  b = =
  is the instantaneous SNR on the k-th channel. Because b can be seen as a chi-square
  Distributed random variable with 2L degrees of freedom ,The pdf P(b) is :
  P(b) =
  Here is the average SNR per channel .

## Slide 25: Theoretical BER
Closed-Form BER Analysis and Diversity Order for Zero Forcing (ZF) Solutions:
  To obtain BER, we need to average the conditional error probability:
  P2 = P (b) d
  There is closed-form solution for this integral, which can be expressed as :
  P2 = [(1 - ) ]L [ (1 + ) ]K
  where

## Slide 26: Theoretical BER
Closed-Form BER Analysis and Diversity Order for Zero Forcing (ZF) Solutions:
  The conditional error probability is applicable for s = - and this leads to a total error probability of P2 /2 + P2 /2 = P2 ,when satisfy the condition >>1, the term (1 + )/2 1 and the term (1- ) , Furthermore,
  =
  Therefore , when is sufficiently large : P2
  Error rate decreases inversely L-th Power of the SNR
  So error rate decreases with an L-th order of diversity

## Slide 27: Theoretical BER
Closed-Form BER Analysis and Diversity Order for Zero Forcing (ZF) Solutions:
  It is shown that the diversity order of an (Nt,Nr) system based on ZF is equal to Nt - Nr + 1.
  Substituting L = Nt - Nr + 1 gives the exact BER for a ZF solution of an (Nt,Nr) system with BPSK.
  If represents the SNR per receiving antenna, the SNR per channel equals :
  c =

## Slide 28: The Minimum Mean Square Error solution
In estimation theory, Estimating a random variable s based on observations x
Choose a function g(x) that minimizes the Mean Square Error
E [(s – sest)*(s- sest) ] = [(s – g(x))* (s-g(x))]
Using linear processing, the estimates of s can be found by
sest = Dx
D must be chosen such that the Mean Square Error is minimized
E [(s – sest)*(s- sest) ] = E[(s – Dx)* (s- Dx)]
E[(s – Dx)* (s- Dx)] = tr(E[(s – Dx)* (s- Dx)] )
= tr(Qs – QsxD* - DQxs + DQxD*)
Where Qs = E[ss*], Qsx = E[sx*], Qxs = E[xs*] and Qx = E[xx*]

## Slide 29: The Minimum Mean Square Error solution
Remark that the covariance matrices are Hermitian: Q = Q*
Proof)
Let Q = E[aa*]
So, Q* = (E[aa*])* = E[(aa*)*] = E[ (a*)* a* ] = E[a*a ] = Q
Remark that the covariance matrices are nonnegative definite
Proof)
z Q z* = z E[aa*] z* = E[z*a a*z] = E[] 0
Furthermore, remark that each eigenvalue of a nonnegative definite matrix is a nonnegative real number.
Proof)
Let Q be nonnegative definite,
λ be an eigenvalue of Q,

## Slide 30: The Minimum Mean Square Error solution
Let z be be an eigenvector of Q associated with λ
So, z* Q z = z* λ z = λ |z|2
Therefore z*Q z / |z|2 is real and nonnegative since it is a ratio of a real nonnegative and a real positive number.
Finally, remark that the eigenvectors of a Hermitian matrix Q, if they come from different eigenvalues, are orthogonal to one another.
Proof)
Qx = λ1 x and Qy = λ2 y and Q = Q* where x and y are the eigenvectors for the eigenvalues λ1 and λ2, respectively.
Then (λ1x)*y = (Qx)* y = x* Qy = x* (λ2y)
We can write λ1 x*y = λ2 x* y Now we use the assumption λ1 λ2, which forces the conclusion that x*y = 0, which again shows that x and y are orthogonal.
The eigenvectors have been normalized to have length one. Since they were already orthogonal, they are now orthonormal.

## Slide 31: The Minimum Mean Square Error solution
If these orthonormal eigenvectors are chosen to be the columns of U
Then we have U* Q U = , where is a diagonal matrix with the eigenvalues of Q on the diagonal and U is said to be a unitary matrix.
we see that we may write Qx as follows:
Qx = U*xU = U*x1/2 x1/2U = (x1/2 U)* (x1/2 U) = A * A
Finally, we can rewrite the MMSE problem to a form, from which a solution for D can be obtained that minimizes the Mean Square Error:
= tr(Qs – QsxD* - DQxs + DQxD*)
= tr(Qs – Qsx A A-1D* - D A* A*-1 Qxs + DA*AD*)
= tr(Qs – Qsx A-1 A*-1 Qxs + Qsx A-1 A*-1 Qxs – Qsx A A-1D* - D A* A*-1 Qxs + DA*AD*)
=tr(Qs – Qsx A-1 A*-1 Qxs +(DA* - Qsx A-1 )(DA* - Qsx A-1 )*)

## Slide 32: The Minimum Mean Square Error solution
Because the first and the second term of this result do not depend on D, the result is minimized if:
  DA* - Qsx A-1 = 0
  DA* = Qsx A-1
  D = Qsx A-1 A*-1 = (A*A) -1 = Qsx Qx-1
Our channel model (x =Hs + v) and assume that Qs =E[ss*] = and Qv = E[vv*] =
And that Qx = E[xx*] = HQsH* + Qv is invertible
Then with Qsx = E[sx*] = E[s(s*H* + v*)] = QsH*
D becomes D = QsH*(HQsH* + Qv)-1 = H*(HH* + ) = H*(HH* + )-1 ,
Where = /

## Slide 33: The Minimum Mean Square Error solution
When using the Matrix Inversion Lemma and demanding that Qs and Qv must be invertible and D can be rewritten as follows:
D = QsH*(Qv + HQsH* )-1 = QsH*(Qv-1 - Qv-1 H(H* Qv-1 H + Qs-1)-1 + H* Qv-1)
= (QsH* Qv-1 – QsH* Qv-1 H (H* Qv-1 H + Qs-1)-1)H* Qv-1
= (Qs(H* Qv-1 H + Qs-1)-Qs H* Qv-1 H ) (H* Qv-1 H + Qs-1)-1 H* Qv-1,
= (H* Qv-1 H + Qs-1)-1 H* Qv-1 = (H*H + I)-1 H* = H*(HH* + )-1
Where = / 0.
If = 0 we obtain the zero-forcing solution.
So, it must be equal to : D = H*(HH* + )-1, 0
Where is equal to / =
It becomes clear that the ZF solution corresponds to an MMSE solution with

## Slide 34: Zero Forcing with Decision Feedback Decoding
Superior performance can be achieved by symbol cancellation
Symbol cancellation involves:
  Decoding the most reliable element first.
  Improving decoding of other elements.
Linear nulling (ZF or MMSE) used for detection.
Decision Feedback Decoding (DFB) is analogous to decision feedback equalization.
DFB modifies the receiver vector by subtracting interference from already detected components.
When symbol cancellation is used components of s are detected becomes important to the overall performance of the system.

## Slide 35: Zero Forcing with Decision Feedback Decoding
To determine a good ordering of detection
The covariance matrix of the estimation error s - Sest will be used
For ZF, this covariance matrix can be shown
2
Or using the pseudo-inverse:

## Slide 36: Zero Forcing with Decision Feedback Decoding
Let (sest)i be the i-th entry of sest
The best estimate (sest)i, is the one for which Pii is the smallest
Estimate with the smallest error covariance
Pii is equal to the squared length of the i-th row of the pseudo-inverse
The minimum squared length row of H+ is equivalent
The pseudo-inverse of H is arranged such that the row with the least squared length becomes the last row
Then the Nt-th element of Sest can be independently decoded
Let Nt denote the decode value
The value can be used to improve the estimate of the remaining Nt signals

## Slide 37: Zero Forcing with Decision Feedback Decoding
Best estimate is performed in a recursive way
The so-called Optimal Detection (OD) method as described
Compute H+
Find the minimum squared length row of H+ and permute it to be the last row, permute the columns of H accordingly.
Form the estimate of the last component of s. In case of ZF: where the transpose of is said to be the Nt - th nulling vector ;
Obtain Nt , (via slicing) from (Sest) Nt ;
(While Nt -1> 0) go back to step 1, but now with:
Note that in case step 2 is skipped, the DFB algorithm is performed without optimal
detection and the overall performance will be less; however , processing time is saved.

## Slide 38: MMSE with Decision Feedback Decoding
In order to perform Decision Feedback Decoding with Minimum Mean Square Error decoding
The covariance matrix of the estimation error will be used

## Slide 39: MMSE with Decision Feedback Decoding
Note that P is somewhat different from the case where ZF is used as detection.
The DFB algorithm is adapted and becomes:
Compute D (P is obtained while computing D);
Find the smallest diagonal entry of P and suppose this is the i-th entry, Permute the i-th column of H to be the last column and permute the rows of D accordingly;
Form the estimate of the "best" component of s: represents the last row of D and its transpose is the Nt-th nulling vector.
Obtain Nt from (sest)Nt ;
(While Nt -1 > 0) go back to step 1, but now with:

## Slide 40: Calculus problem
=
=

## Slide 41: MIMO with CSIT – Joint SVD
By svd, are singular vector matrices corresponding to non-zero singular values in .
For joint svd, we set for positive diagonal matrix and
W
Q1) Specify the dimension of ?
Q2) Show that

## Slide 42: Assignment-07
1. MIMO linear processing
MIMO without CSIT
  2)RxMF
  3)RxZF
  4)RxMMSE
MIMO with CSIT
  5) Joint SVD
6)Numerical result

## Slide 43: MIMO with linear processing
Let follow zero-mean complex Gaussian distribution
Define

## Slide 44: MIMO with linear processing
Q1) Specify the dimension of
Solution)
Q2)Write an expression of the post-Processed signal in terms of
Solution)
Q3) Show that

## Slide 45: MIMO with linear processing
Q4) Show that the capacity is expressed by
|

## Slide 46: MIMO without CSIT – RxMF
Q1) Show that and
Solution)

## Slide 47: MIMO without CSIT – RxMF
Q2) Show that and
Solution)
We know that )
]

## Slide 48: MIMO without CSIT – RxMF
Also
Q3) Letting show that
Solution)
Q4) Letting show that
Solution)

## Slide 49: MIMO without CSIT – RxMF
For simplicity , we let and such that
Q5) Show that
The capacity is expressed by
|
|
|

## Slide 50: MIMO without CSIT – RxMF
Q6)For AWGN , i.e
Show that
Solution)

## Slide 51: MIMO without CSIT – RxZF
From and using standard basis vectors in which the element is 1 and the other elements are 0.
Using the method of Lagrangian multipliers
Q1) Show that

## Slide 52: MIMO without CSIT – RxZF
We know that
)
=

## Slide 53: MIMO without CSIT – RxZF
Q2) Show that
+ 0
=

## Slide 54: MIMO without CSIT – RxZF
Q3)Letting
Solution)

## Slide 55: MIMO without CSIT – RxZF
Q4) Letting and show that
So,
and
So that
Q5) Show that
Solution)

## Slide 56: MIMO without CSIT – RxZF
Q6) Show that
Solution)
Here,
Q7) For AWGN ,i.e show that
Solution)

## Slide 57: MIMO without CSIT – RxMMSE
We minimize the mean square error (MSE) between
Thus , we solve the following problem:
Q1) Show that
Solution)
Here

## Slide 58: MIMO without CSIT – RxMMSE
Since this is an unconstrained convex problem , the optimal solution is stationary point with
Q2) Show that
We know that

## Slide 59: MIMO without CSIT – RxMMSE
Q2) Letting show that
Solution)

## Slide 60: MIMO without CSIT – RxMMSE
Q4) Using the Woodbury matrix identity also show that
Solution)
We know that
)

## Slide 61: MIMO without CSIT – RxMMSE
5) If rank(P) = Ns , Using , show that
Here
So ,we can write
|
|
|
|
|

## Slide 62: MIMO without CSIT – RxMMSE
6) if rank for AWGN i.e show that
We can write
Just plugging the we can write

## Slide 63: MIMO with CSIT – joint SVD
By SVD, where and are singular vector matrices corresponding to non-zero singular values in
For joint SVD,
We set for positive diagonal matrix and
Q1) Specify the dimension of
Let's denote the dimension,
Let be a positive diagonal matrix of size (where is the number of selected singular values)

## Slide 64: MIMO with CSIT – joint SVD
is obtained by selecting the columns corresponding to the non-zero singular values from and it is size of
So =
is a square diagonal matrix of size containing the non-zero singular values.
So =
is obtained by selecting the columns corresponding to the non-zero singular values from and it is size of
is obtained by selecting the columns corresponding to the zero singular values from
and it is of size
So,
is obtained the selecting the columns corresponding to the non-zero singular values from and it is of size
So =

## Slide 65: MIMO with CSIT – joint SVD
2) Show that
Solution)
We can write

## Slide 66: MIMO with CSIT – joint SVD
3) Show that
Solution)

## Slide 67: MIMO with CSIT – joint SVD
4)For AWGN, i.e , , Show that i.e achieving the MIMO capacity when are optimized.
Solution)
Capacity is expressed by
But here , and
So, plugging those values in capacity equation we can write,

## Slide 68: MIMO with CSIT – joint SVD
Q1

## Slide 69: MIMO with CSIT – joint SVD
5)Letting for RxMF , RxZF, RxMMSE show that becomes equivalent to the case with CSIT, i.e achieving the MIMO capacity when are optimized.
Solution)
For AWGN, Capacity for RxMF , RxZF, RxMMSE is
which is equivalent to the case with csit i.e
when are optimized.

## Slide 70: MIMO with CSIT – joint SVD
In the absence of the CSIT, one possible design for the precoder is
Such that average transmit energy is equally distributed to the symbols and by assigning to Txi’s in order. antenna are unused.
Q1) Show that
Solution)

## Slide 71: SIMO
Let follow zero-mean complex Gaussian distributions.
Define
Q1) Specify the dimension of H, W
Solution)

## Slide 72: SIMO
Q2) Write an expression of the post-processed signal in terms of
Solution)
Q3) Show that capacity is expressed by
Solution)
We know that

## Slide 73: SIMO
So now we can write

## Slide 74: SIMO
)

## Slide 75: SIMO
Q5) For AWGN, i.e,
Solution)

## Slide 76: SIMO
Q6)Using the Cauchy-Schwartz inequality ,Find the optimal that maximizes and showthat the maximum capacity is
Solution)
From Cauchy-Schwartz inequality we can write
Let
Then

## Slide 77: SIMO
For the estimated symbol is

## Slide 78: SIMO

## Slide 79: MISO
Let
Q1) Specify the dimension of P , H
Solution)

## Slide 80: MISO
Q2) Write an expression of the post-processed signal in terms of
Q3) Show that average transmit energy
Solution)

## Slide 81: MISO
Q4) Show that the capacity is expressed by
Solution)

## Slide 82: MISO

## Slide 83: MISO
First Approach : We design such that the average transmit energy is equally distributed to the antennas , i.e
(Equal power allocation)
Q5) Show that the capacity is
Solution)

## Slide 84: MISO
Second approach: We design such that the average transmit energy is concentrated by assigning are unused.
Q6) Show that the capacity is
Solution)

## Slide 85: MISO
In this case , we can optimize the precoder P to achieve the maximum capacity P
Q1) Using the Cauchy-Schwartz inequality find the optimal P that maximizes with
Show that maximum capacity is

## Slide 86: MISO
Solution)
Applying the Cauchy-Schwartz inequality
Let
Substituting the

## Slide 87: MISO
Q2)Show that MRT achieves the maximum capacity
Solution)

## Slide 88: MISO

## Slide 89: MISO

## Slide 90: SISO
Assume
Q1) Write an expression of the received signal in terms of
Solution)

## Slide 91: SISO
Q2) Show that the average transmit energy is
Solution)
Q3) Show that the capacity is expressed by
Solution)

## Slide 92: SISO

## Slide 93: SISO

## Slide 94: MIMO with DFB(V-BLAST)
Let , and follow zero mean Gaussian distributions.
Define
We successively cancel the interference by already detected components of x from the received signal y.
The order in which the components of x are detected becomes important to the overall performance.

## Slide 95: MIMO with DFB(V-BLAST)
Q1) Show that
Solution)
)

## Slide 96: MIMO with DFB(V-BLAST)
2) Show that represent the MSE of the i-th symbol
Solution)
3) Show that obtaining again with is equivalent to obtaining
with
Solution)

## Slide 97: MIMO with DFB(V-BLAST)
We then decode with the smallest as
After that, by noting
We exclude the interference by from
We calculate again with and determine the next symbol to decode
After updating and , the covariance matrix becomes :
This represent the MSE between the transmitted symbols and the estimated symbols , considering the exclusion of the interference caused by the previously decoded symbol

## Slide 98: MIMO with MF-DFB
1) Show that
Solution)
)
For MF
)

## Slide 99: MIMO with ZF-DFB
)
For ZF
=

## Slide 100: MIMO with ZF-DFB

## Slide 101: MIMO with MMSE-DFB
)
For MMSE