## Slide 1: Active Jamming for AF Relay-Based Covert Communications
Refat Khan, Jihwan Moon
Cognitive Communications System Lab
School of Electrical Engineering
Hanbat National University
2024 KIEES Radio Science and Communication Conference
Oct 25, 2024

## Slide 2: Introduction
Wireless Communication
  Securing Wireless Communication
    Wireless technology transforms lives, but cyberattacks pose a threat, leading to potential information leaks
    To cope with this, cryptography has widely been adopted.
  The perspective of physical layer security
    Yet, cryptography has limitations: complex key generation and susceptibility to
    powerful eavesdroppers, especially challenging for IoT devices.
    These downsides have led researchers to examine the possibility of utilizing physical layer security
An approach of secure communications: Covert Communication
  Covert communication
    Opponents can conduct traffic analysis by collecting metadata during transmission.
    Vulnerabilities include capturing source and destination addresses, request-response frequency, etc.
Introduction
Alice
Bob
Eve

## Slide 3: Introduction
An approach of secure communications: Covert Communication
  Need for Covert Communications
    Transmit data in a manner that avoids detection or suspicion.
    Combining cryptography and physical layer security can prevent eavesdropping, but covert communications are necessary to counter traffic analysis threats.
Unveiling Covert Communication: AF Relay System
AF Relay :
  Simple Implementation, and it does not need to decode or interpret the signal.
  It simply scales and forwards the received signal
Stealth Strategy:
  Covert message with public message
  Using artificial noise
Optimization Goal:
  Maximize covert rate, minimize detection
Introduction
Carol
Bob
Alice
Willie

## Slide 4: System Model
Source
S
Covert message, xC
Artificial
noise, xJ
AF Relay
R
Public message, xP
Covert message detector
Destination
D
2.1 Schematic Diagram
Figure 1. System Model
System Model Problem Formulation Numerical Result

## Slide 5: System Model
2.2 Received signals
  At the AF relay
    : Public message, covert message and artificial noise, respectively
    : Transmit power at the source
    : Transmit power allocation for and , respectively, at the source
    : Uniform transmit power allocation in dB for at the source
      dB
Source
S
AF relay
R
Public message,
System Model Problem Formulation Numerical Result

## Slide 6: System Model
2.2 Received signals
  At the destination
AF relay
R
Destination
D
System Model Problem Formulation Numerical Result

## Slide 7: System Model
2.2 Received signals
  At the destination
    Achievable rate for the public message by treating the covert message as interference
System Model Problem Formulation Numerical Result

## Slide 8: System Model
2.2 Received signals
  At the destination
    Achievable rate for the covert message after canceling the decoded public message and artificial noise by cooperation between and to have
Cancellable by cooperation between and
System Model Problem Formulation Numerical Result

## Slide 9: Problem Formulation
Covert rate maximization
  Objective function
    Covert rate
  Constraint 1
    Minimum public rate threshold
      The worst-case with
  Constraint 2
    Minimum DEP threshold
  Constraint 3
    To avoid zero DEP
  Constraint 4
    The sum of power proportion
  Constraint 5
    Maximum artificial noise power bound
  Constraint 6
    Individual power proportion
System Model Problem Formulation Numerical Result

## Slide 10: Numerical Result
System parameter
System Model Problem Formulation Numerical Result

## Slide 11: Numerical Result
Node Location
System Model Problem Formulation Numerical Result

## Slide 12: Numerical Result
Source transmit power,
Figure 2. Source transmit power vs average covert rate
Figure 3. Source transmit power vs average power proportion
Figure 2. depicts the average covert rate in relation to the source transmission power.
The results shows that the optimal solution achieves the highest performance improvement.
In contrast to the other schemes where either artificial noise mean or the fluctuation bound .
In Figure 3. we observe that source transmit power does not affect on noise mean .
System Model Problem Formulation Numerical Result