## Slide 1: Covert Communication for a Disguised Full-Duplex vehicle with channel Distribution Information
2024.02.01
KICS Winter Conference 2024
Refat Khan, *Jihwan Moon
Department of Mobile Convergence Engineering, Hanbat National University

## Slide 2: Table of Contents
Introduction
Method
Numerical Result
Conclusion

## Slide 3: Introduction
Challenges of Secure Communication:
Security Threats:
  Opponents can conduct traffic analysis by collecting metadata during transmission.
  Vulnerabilities include capturing source and destination addresses, request-response frequency, etc
Need for Covert Communications:
  Transmit data in a manner that avoids detection or suspicion.
  Combining cryptography and physical layer security can prevent eavesdropping, but covert communications are necessary to counter traffic analysis threats.

## Slide 4: Introduction
Investigating Covert Communications:
System Overview:
  Setup involves a source vehicle and disguised full-duplex (FD) destination vehicle.
Objective:
  Ensure covert transmission to a hidden vehicle while warden vehicle surveillance.
Research Scope:
  Explore channel uncertainty at the warden vehicle.
  Determine the lower bound of the expected minimum detection error probability (DEP).
Research Outcomes:
  Numerical results demonstrating covert rate performance under diverse DEP requirements
  Emphasis on the significance of secure and covert communication strategies against advanced security threats.

## Slide 5: Method
Figure. Node Placement

## Slide 6: Method
Covert Communication System Overview:
Communication Setup:
  Source vehicle (S) transmitting a public message to the destination vehicle (D)
  Covert transmission conducted by the seemingly receive-only destination vehicle
  Covert signal transmitted to the hidden vehicle (R) using an unseen antenna
Transmission Environment:
  Full-duplex (FD) communication implemented, allowing simultaneous transmission and reception
  Warden vehicle (W) monitoring for suspicious communications
Key Focus:
  Ensuring secure and undetectable transmission from the destination to the hidden vehicle
  Under surveillance of a warden vehicle

## Slide 7: Method
Received Signal in Covert Communication:
The received signal at the disguised full-duplex (FD) destination can be expressed as
Signal Information :
  'Public message' denoted as xP CN(0,1) and 'covert message' denoted as xc CN(0,1)
  'Transmit power' at the destination indicated PD as and at the source as PS
Noise and Interference:
  'Residual self-interference channel' represented by CN(0, ) , accounting for residual signal interference
  ZX CN(0, ) 'Additive noise' at node X, reflecting the presence of additional background noise.

## Slide 8: Method
Channel Uncertainty in Transmission:
Consideration of Uncertainty:
  The channel uncertainty of the D-W link, and hDW can be modelled as
  hDW = +
Model Representation:
  Channel uncertainty can be effectively modeled as a combination of ground-truth channel (hDW), estimated channel (), and estimation error CN(0,LDW)
  [0,1] denotes the level of estimation, aiding in understanding the accuracy of the estimation process

## Slide 9: Method
Calculating Achievable Public Data Rate:
Data Rate Calculation:
=
  The achievable public data rate () is determined as a logarithmic function.
  It is calculated based on the ratio of the squared magnitude of the channel from the source to the destination () and the estimated squared magnitude of the channel at the destination ().
  The calculation also considers the source power (), destination power (), and the variance of the noise ().

## Slide 10: Method
Signal Reception and Decoding at Hidden Receiver:
Signal Reception:
            yR = hSR + + zR
  Hidden vehicle (R) receives both a direct-link public message from the source vehicle and a covert message from the destination vehicle.
  The received signal (yR) is a composite of these public and covert messages, along with additional noise (zR).
Decoding Process:
  The hidden vehicle decodes and separates the public messages, eliminating them to isolate the covert messages.
  Signal processing techniques are applied to recover and extract the covert communication from the received signal.

## Slide 11: Method
Limitations of Public Data Rate for Decoding Constraint:
It is required that the public data rate be limited by its achievable amount:
r̅PR =
  The achievable public data rate (r̅PR) follows a logarithmic function.
  Calculation relies on () and (), the squared magnitudes of the source-to-hidden receiver and destination-to-hidden receiver channels.
  The calculation also considers the source power (), destination power (), and the variance of the noise at the receiver ().

## Slide 12: Method
Covert Rate Calculation:
Achievable Covert Rate:
rCR =
  Covert rate(rCR) after removing 𝑥𝑃 from 𝑦R
  Calculation relies on (), the squared magnitudes of the destination-to-hidden receiver channel and the variance of the noise at the receiver ().
Significance:
  Understanding the covert rate aids in evaluating the efficiency of covert communication channels
  Highlighting the impact of signal manipulation on achieving secure communication

## Slide 13: Method
During Communication Warden vehicle receives
Warden vehicle knows perfectly necessary parameter
Such as
Worst-case assumption :
Null and alternative hypotheses :
The asymptotic test statistic T for the hypothesis as N is
For H0 : T =
For 𝐻1: 𝑇 = |ℎ𝐷𝑊|²𝑃𝐷 + 𝜎𝑊²

## Slide 14: Method
Covert Message Detection: 𝑇 ≥ 𝜏 (Detected), 𝑇 < 𝜏 (Not Detected)
    Uncertainty in Noise Variance 𝜎𝑅² :
    𝜎𝑊,dB² ~ 𝑈(𝜎̅𝑊,dB² − dB, 𝜎̅𝑊,dB² + dB)
    𝜎̅𝑊,dB²: Mean Value, 𝜁dB>0: Maximum Range
The resulting DEP Pr(e) is calculated by
that minimizes the DEP is obtained from
Resulting DEP becomes

## Slide 15: Method
Optimize the following problem
Exact expectation of DEP is analytically intractable
Jensen's inequality is employed due to the concavity of the logarithm
Lower bound of the expected DEP

## Slide 16: Numerical Result
Figure. Average covert rate vs DEP threshold
The graph illustrates the average worst-case covert rate under perfect and imperfect CSI conditions as the minimum DEP threshold varies.
It emphasizes the significance of acquiring reliable CSI for optimal performance.

## Slide 17: Conclusion
Quality CSI is indispensable for minimizing the Detection Error Probability (DEP) at the AF relay.
Accurate CSI facilitates optimal signal processing, enhancing the reliability and effectiveness of covert communication strategies.
High-quality CSI ensures robust covert communication, strengthening the security and efficiency of the system.

## Slide 18
Thank you for your Listening. For any queries, please email me at: refatkhanuits@gmail.com