## Slide 1: Space Division Multiplexing combined with OFDM
REFAT KHAN

## Slide 2: Table of Contents
Broadband Wireless Communication Systems
Impact of Receiver diversity techniques
Some Diversity techniques
    Frequency and Time diversity
    Space diversity
    Polarization diversity
    Selection diversity
    Maximal Ratio and Equal Gain Combining
Multi-Antenna Link: Signal model and SDM techniques
Signal model

## Slide 3: Broadband Wireless Communication Systems
One example of a broadband wireless communication system is a wireless computer
network. Wireless computer networks are in demand in offices and universities.
Another example of a broadband wireless communication system is a wireless
communication system that uses Space Division Multiplexing (SDM). SDM is a technique
that transmits different data streams on different transmit antennas simultaneously.
This thesis will compare a number of SDM algorithms and combine the best algorithm
with Orthogonal Frequency Division Multiplexing (OFDM) to avoid Inter Symbol
Interference (ISI).

## Slide 4: Impact of Receiver diversity techniques
Before SDM techniques were developed, receiver diversity was seen as a powerful communication receiver technique that provided wireless link improvement at relatively low cost.
Diversity techniques try to solve the problem that transmission errors occur when the transmission channel attenuation is large, i.e., when the channel is in a deep fade.

## Slide 5: Frequency and Time diversity
Frequency diversity is a technique that improves the performance of wireless systems by transmitting the same signal on multiple frequencies. The receiver then selects the frequency that has suffered least from fading or combines the signals from all frequencies to improve the estimation of the transmitted signal.
Time diversity transmits the same signal multiple times, with a time spacing between transmissions that is greater than the coherence time of the channel. This ensures that the multiple repetitions of the signal will be received with independent fading conditions.

## Slide 6: Space diversity
Space diversity, also known as antenna diversity, is a technique that improves the performance of wireless systems by using multiple antennas. The antennas are separated by a distance of half a radio wavelength or more, which ensures that the signals received by the antennas are uncorrelated. This means that if one antenna receives a weak signal, another antenna is likely to receive a strong signal.

## Slide 7: Polarization diversity
In wireless communication, polarization diversity is used to enhance reliability. It involves transmitting the same signal on two antennas with different polarizations, exploiting uncorrelated paths and combining horizontally and vertically polarized signals at the receiver for improved quality. This provides two diversity branches, simplifies antenna placement, but mixing with other diversity methods may degrade performance. The choice of diversity technique depends on the specific communication environment and system requirements.

## Slide 8: Selection diversity
Selection Diversity The highest instantaneous SNR branch is connected to the demodulator.

## Slide 9: Maximal Ratio and Equal Gain Combining
Maximal Ratio combining : Maximum Ratio Combining (MRC) is an optimization technique for combining signals that are carrying the same information.
Equal Gain combining : An Equal Gain Combiner is obtained when the gains used in MRC are all set to unity. The disadvantage is that (like MRC) an individual receiver for each antenna element is needed. However, the possibility of producing an acceptable signal from a number of unacceptable inputs is still retained, and the performance is only marginally inferior to MRC and usually superior to selection diversity.

## Slide 10: Multi-Antenna Link: Signal model and SDM techniques
One way to increase the capacity of wireless communication systems is by exploiting the spatial dimension using multiple antennas at the receiver as well as at the transmitter. This type of transmission is called Space Division Multiplexing (SDM).
In this chapter, a number of different decoding algorithms for SDM will be discussed and their performance will be compared.

## Slide 11: Signal model
We consider a communication system comprising Nt transmit (TX) and Nr receive (RX) antennas that operates in a Rayleigh flat-fading environment and exploits the spatial dimension by using Space Division Multiplexing (SDM).
A channel is said to be a Rayleigh fading channel when the channel impulse response is modelled as a zero-mean complex-valued gaussian process .
In this case, the envelope of the channel impulse response at any time instant has a Rayleigh probability distribution and the phase is uniformly distributed in the interval (0,2p).
This can be shown as follows. Suppose we model the channel impulse response H as a zero-mean complex gaussian variable, like:
H = A + jB

## Slide 12: Signal model
Where A and B are zero-mean statistically independent real guassian variables, each having a variance s2/2. The variance of the complex gaussian variable H can be shown to be:
var(H ) = E[H 2 ]- E[H ]2 = E[(A + jB)(A + jB)] = E[A2 + 2 jAB + B 2 ]= E[A2 ]+ E[B 2 ]= s 2
We introduce a new variable
Y = A2 + B 2
Here Y is chi-squared Random variable

## Slide 13: Signal model
Hence, the probability density function (pdf) of Y is:
pY (y) = e - y / 2 , y 0
Now, suppose we define a random variable R to denote the envelope of the channel impulse response:
R = =
In order to find the pdf of R, we need to make a change of variables in the Probability Distribution Function
(PDF) of Y to first find the PDF of R:
FR(r) = P(R ≤ r) = P(Y ≤ r) = P( ≤ r²) = F(r²)

## Slide 14: Signal model
where the fact is used that r ³ 0. Then the pdf of R is given by
pR® = FR(r) = Fy(r2) = 2 r pY(r2) = e – r 2 / 2 , r 0
This is the pdf of a Rayleigh-distributed random variable; thus, the envelope of H has a Rayleigh probability distribution. The fact that the phase of H is uniformly distributed in the interval (0,2p) .
Suppose that at discrete times, the transmitter sends an Nt-dimensional (complex) signal vector s (i.e., it transmits Nt parallel streams of data), and the receiver records an Nr-dimensional complex vector x. Then the following signal model describes the relation between s and x:
x = Hs + ν
where H is an Nr ´ Nt complex propagation matrix ) and the vector ν (Nr- dimensional) represents additive receiver noise

## Slide 15: Signal model
The vector s is assumed to have zero-mean, uncorrelated random variables with variance equal to ss2. The vector s is assumed to have zero-mean, uncorrelated random variables with variance equal to ss2. The total power of s (i.e., E[s*s]) is assumed to be P. Thus, the covariance matrix of s equals:
E[s*s] = ss2 INt = INt
Where * denotes the conjugate transpose of a vector or matrix and the matrix I with subscript Nt represents the identity matrix with dimension Nt
The channel matrix is denoted by H. It is assumed the channel matrix H has independently and identically distributed (i.i.d.), zero-mean, complex Gaussian, unit variance entries (the variance of each entry is sc2 = 1). In other words, each component has a Rayleigh distribution (like H) with s2 = sc2 = 1. Thus, the system operates in a Rayleigh flat-fading environment.

## Slide 16: Signal model
The vector ν is Nr-dimensional and represents additive receiver noise. The vector ν is assumed to have zero-mean, uncorrelated random variables with variance sn2 and a covariance matrix equal to:
E[v*v] = sv2 INt
Furthermore, it is assumed that the vectors s and ν are independent and thus the following holds: E[sν* ] = 0 . With the above-described assumptions about the power of the signal and the noise, the expected Signal-to- Noise Ratio (SNR) per receiving antenna, i.e., the SNR for each component of x, can be found and is equal to
= = =
Where Es stands for the signal power per receive antenna and N0 denotes the noise power per receive antenna.

## Slide 17: Signal model
In order to explain the different Space Division Multiplexing techniques, the following notations will be used
where xi and si represent the i-th element of x and s respectively. Hi and hi denote the i-th row and i-th column of H, respectively.
In the following sections, a number of SDM decoding techniques for the receiver will be discussed and compared.

## Slide 18: The Zero Forcing Algorithm
Zero Forcing Algorithm in Adaptive Antenna Array (AAA):
  Zero Forcing algorithm is based on a conventional adaptive antenna array (AAA) technique.
  Known as linear combinatorial nulling
  Each sub stream is the desired signal.
  The remaining data streams are considered as "interferers“.
  Nulling of the "interferers" can be performed by choosing weight vectors di (with i =1,2, ..., Nt) such that
  Where T stands for transpose of a matrix.
  And stands for j-th column of the channel matrix H.

## Slide 19: The Zero Forcing Algorithm
Zero Forcing Algorithm in Adaptive Antenna Array (AAA):
  Solving the weight vectors is equal to finding a matrix D such that :
  D * H = I
  Where D is a matrix that represents the linear processing in the receiver.
  Forcing the ‘’interference’’ to zero , S is estimated
  If H is not square, then D equals the pseudo-inverse of H:
  D = H+ = (H*H)-1 H*
  Where + represent the pseudoinverse.
  Some constraint for Pseudo-inverse
    Nt Nr
    The column of H must be independent

## Slide 20: The Zero Forcing Algorithm
Zero Forcing Algorithm in Adaptive Antenna Array (AAA):
  If the inverse is the exists, the estimates of S can be found by:
    Sest = Dx
    = (H*H)-1 H* x
    Or equivalently:
    Sest = H+ x
  And for i-th Sest can be written as :
  (Sest)i = Hi+ x
  Hi+ represent the i-th row of H+ , is equal to the transpose of the i-th weight vector di
  di is the so-called nulling vector.

## Slide 21: The Zero Forcing Algorithm
Zero Forcing Algorithm in Adaptive Antenna Array (AAA):
  The ZF algorithm's performance can be tested through simulations, and its behavior can be theoretically understood by comparing it with the MRC system.
  Understanding the diversity order helps relate the ZF algorithm to the MRC system.
  This comparison gives valuable insights into the ZF algorithm's performance, making it crucial for evaluating wireless systems.

## Slide 22: Theoretical BER
System Operation and Decision Variable in Raleigh Flat-Fading Environment for BPSK:
  In a system operating under Raleigh flat-fading, the channel elements can be expressed for an MRC system with one transmit and L receive antennas
  The channel characteristics in the MRC system are determined by the channel elements , channel attenuation factor , and phase shift , assuming perfect channel knowledge.
  The system output in a Raleigh flat-fading environment is represented by a single decision variable U for BPSK with Lth-order diversity:
  U = Re ( xk ) = Re ( s + vk )
  Where vk denotes the complex gaussian noise and s is the transmitted symbol.

## Slide 23: Theoretical BER
Probability and SNR Analysis for BPSK in Flat-Fading Channels:
  For BSPK, The decision variable U is used in the decoder to recover the transmitted s.
  If U> 0 then s = and U < 0 then s = -
  For a fixed set of {} and the assumption that s = is transmitted.
  The Gaussian decision variable U, with mean noise power N0 per receive antenna, determines the probability of being less than zero is :
  P2 (b) = Q() where Q is the function as : Q(x) = dt and x

## Slide 24: Theoretical BER
BER Analysis and Error Rate Behavior with L-th Order Diversity in Flat-Fading Channels:
  The SNR per bit , b is given as :
  b = =
  is the instantaneous SNR on the k-th channel. Because b can be seen as a chi-square
  Distributed random variable with 2L degrees of freedom ,The pdf P(b) is :
  P(b) =
  Here is the average SNR per channel .

## Slide 25: Theoretical BER
Closed-Form BER Analysis and Diversity Order for Zero Forcing (ZF) Solutions:
  To obtain BER, we need to average the conditional error probability:
  P2 = P (b) d
  There is closed-form solution for this integral, which can be expressed as :
  P2 = [(1 - ) ]L [ (1 + ) ]K
  where

## Slide 26: Theoretical BER
Closed-Form BER Analysis and Diversity Order for Zero Forcing (ZF) Solutions:
  The conditional error probability is applicable for s = - and this leads to a total error probability of P2 /2 + P2 /2 = P2 ,when satisfy the condition >>1, the term (1 + )/2 1 and the term (1- ) , Furthermore,
  =
  Therefore , when is sufficiently large : P2
  Error rate decreases inversely L-th Power of the SNR
  So error rate decreases with an L-th order of diversity

## Slide 27: Theoretical BER
Closed-Form BER Analysis and Diversity Order for Zero Forcing (ZF) Solutions:
  It is shown that the diversity order of an (Nt,Nr) system based on ZF is equal to Nt - Nr + 1.
  Substituting L = Nt - Nr + 1 gives the exact BER for a ZF solution of an (Nt,Nr) system with BPSK.
  If represents the SNR per receiving antenna, the SNR per channel equals :
  c =

## Slide 28: The Minimum Mean Square Error solution
In estimation theory, Estimating a random variable s based on observations x
Choose a function g(x) that minimizes the Mean Square Error
E [(s – sest)*(s- sest) ] = [(s – g(x))* (s-g(x))]
Using linear processing, the estimates of s can be found by
sest = Dx
D must be chosen such that the Mean Square Error is minimized
E [(s – sest)*(s- sest) ] = E[(s – Dx)* (s- Dx)]
E[(s – Dx)* (s- Dx)] = tr(E[(s – Dx)* (s- Dx)] )
= tr(Qs – QsxD* - DQxs + DQxD*)
Where Qs = E[ss*], Qsx = E[sx*], Qxs = E[xs*] and Qx = E[xx*]

## Slide 29: The Minimum Mean Square Error solution
Remark that the covariance matrices are Hermitian: Q = Q*
Proof)
Let Q = E[aa*]
So, Q* = (E[aa*])* = E[(aa*)*] = E[ (a*)* a* ] = E[a*a ] = Q
Remark that the covariance matrices are nonnegative definite
Proof)
z Q z* = z E[aa*] z* = E[z*a a*z] = E[] 0
Furthermore, remark that each eigenvalue of a nonnegative definite matrix is a nonnegative real number.
Proof)
Let Q be nonnegative definite,
λ be an eigenvalue of Q,

## Slide 30: The Minimum Mean Square Error solution
Let z be be an eigenvector of Q associated with λ
So, z* Q z = z* λ z = λ |z|2
Therefore z*Q z / |z|2 is real and nonnegative since it is a ratio of a real nonnegative and a real positive number.
Finally, remark that the eigenvectors of a Hermitian matrix Q, if they come from different eigenvalues, are orthogonal to one another.
Proof)
Qx = λ1 x and Qy = λ2 y and Q = Q* where x and y are the eigenvectors for the eigenvalues λ1 and λ2, respectively.
Then (λ1x)*y = (Qx)* y = x* Qy = x* (λ2y)
We can write λ1 x*y = λ2 x* y Now we use the assumption λ1 λ2, which forces the conclusion that x*y = 0, which again shows that x and y are orthogonal.
The eigenvectors have been normalized to have length one. Since they were already orthogonal, they are now orthonormal.

## Slide 31: The Minimum Mean Square Error solution
If these orthonormal eigenvectors are chosen to be the columns of U
Then we have U* Q U = , where is a diagonal matrix with the eigenvalues of Q on the diagonal and U is said to be a unitary matrix.
we see that we may write Qx as follows:
Qx = U*xU = U*x1/2 x1/2U = (x1/2 U)* (x1/2 U) = A * A
Finally, we can rewrite the MMSE problem to a form, from which a solution for D can be obtained that minimizes the Mean Square Error:
= tr(Qs – QsxD* - DQxs + DQxD*)
= tr(Qs – Qsx A A-1D* - D A* A*-1 Qxs + DA*AD*)
= tr(Qs – Qsx A-1 A*-1 Qxs + Qsx A-1 A*-1 Qxs – Qsx A A-1D* - D A* A*-1 Qxs + DA*AD*)
=tr(Qs – Qsx A-1 A*-1 Qxs +(DA* - Qsx A-1 )(DA* - Qsx A-1 )*)

## Slide 32: The Minimum Mean Square Error solution
Because the first and the second term of this result do not depend on D, the result is minimized if:
  DA* - Qsx A-1 = 0
  DA* = Qsx A-1
  D = Qsx A-1 A*-1 = (A*A) -1 = Qsx Qx-1
Our channel model (x =Hs + v) and assume that Qs =E[ss*] = and Qv = E[vv*] =
And that Qx = E[xx*] = HQsH* + Qv is invertible
Then with Qsx = E[sx*] = E[s(s*H* + v*)] = QsH*
D becomes D = QsH*(HQsH* + Qv)-1 = H*(HH* + ) = H*(HH* + )-1 ,
Where = /

## Slide 33: The Minimum Mean Square Error solution
When using the Matrix Inversion Lemma and demanding that Qs and Qv must be invertible and D can be rewritten as follows:
D = QsH*(Qv + HQsH* )-1 = QsH*(Qv-1 - Qv-1 H(H* Qv-1 H + Qs-1)-1 + H* Qv-1)
= (QsH* Qv-1 – QsH* Qv-1 H (H* Qv-1 H + Qs-1)-1)H* Qv-1
= (Qs(H* Qv-1 H + Qs-1)-Qs H* Qv-1 H ) (H* Qv-1 H + Qs-1)-1 H* Qv-1,
= (H* Qv-1 H + Qs-1)-1 H* Qv-1 = (H*H + I)-1 H* = H*(HH* + )-1
Where = / 0.
If = 0 we obtain the zero-forcing solution.
So, it must be equal to : D = H*(HH* + )-1, 0
Where is equal to / =
It becomes clear that the ZF solution corresponds to an MMSE solution with

## Slide 34: Zero Forcing with Decision Feedback Decoding
Superior performance can be achieved by symbol cancellation
Symbol cancellation involves:
  Decoding the most reliable element first.
  Improving decoding of other elements.
Linear nulling (ZF or MMSE) used for detection.
Decision Feedback Decoding (DFB) is analogous to decision feedback equalization.
DFB modifies the receiver vector by subtracting interference from already detected components.
When symbol cancellation is used components of s are detected becomes important to the overall performance of the system.

## Slide 35: Zero Forcing with Decision Feedback Decoding
To determine a good ordering of detection
The covariance matrix of the estimation error s - Sest will be used
For ZF, this covariance matrix can be shown
2
Or using the pseudo-inverse:

## Slide 36: Zero Forcing with Decision Feedback Decoding
Let (sest)i be the i-th entry of sest
The best estimate (sest)i, is the one for which Pii is the smallest
Estimate with the smallest error covariance
Pii is equal to the squared length of the i-th row of the pseudo-inverse
The minimum squared length row of H+ is equivalent
The pseudo-inverse of H is arranged such that the row with the least squared length becomes the last row
Then the Nt-th element of Sest can be independently decoded
Let Nt denote the decode value
The value can be used to improve the estimate of the remaining Nt signals

## Slide 37: Zero Forcing with Decision Feedback Decoding
Best estimate is performed in a recursive way
The so-called Optimal Detection (OD) method as described
Compute H+
Find the minimum squared length row of H+ and permute it to be the last row, permute the columns of H accordingly.
Form the estimate of the last component of s. In case of ZF: where the transpose of is said to be the Nt - th nulling vector ;
Obtain Nt , (via slicing) from (Sest) Nt ;
(While Nt -1> 0) go back to step 1, but now with:
Note that in case step 2 is skipped, the DFB algorithm is performed without optimal
detection and the overall performance will be less; however , processing time is saved.

## Slide 38: MMSE with Decision Feedback Decoding
In order to perform Decision Feedback Decoding with Minimum Mean Square Error decoding
The covariance matrix of the estimation error will be used

## Slide 39: MMSE with Decision Feedback Decoding
Note that P is somewhat different from the case where ZF is used as detection.
The DFB algorithm is adapted and becomes:
Compute D (P is obtained while computing D);
Find the smallest diagonal entry of P and suppose this is the i-th entry, Permute the i-th column of H to be the last column and permute the rows of D accordingly;
Form the estimate of the "best" component of s: represents the last row of D and its transpose is the Nt-th nulling vector.
Obtain Nt from (sest)Nt ;
(While Nt -1 > 0) go back to step 1, but now with:

## Slide 40
Thank Your Listening. Any Questions?