## Slide 1: Space Division Multiplexing combined with OFDM
REFAT KHAN

## Slide 2: Table of Contents
Broadband Wireless Communication Systems
Impact of Receiver diversity techniques
Some Diversity techniques
    Frequency and Time diversity
    Space diversity
    Polarization diversity
    Selection diversity
    Maximal Ratio and Equal Gain Combining
Multi-Antenna Link: Signal model and SDM techniques
Signal model

## Slide 3: Broadband Wireless Communication Systems
One example of a broadband wireless communication system is a wireless computer
network. Wireless computer networks are in demand in offices and universities.
Another example of a broadband wireless communication system is a wireless
communication system that uses Space Division Multiplexing (SDM). SDM is a technique
that transmits different data streams on different transmit antennas simultaneously.
This thesis will compare a number of SDM algorithms and combine the best algorithm
with Orthogonal Frequency Division Multiplexing (OFDM) to avoid Inter Symbol
Interference (ISI).

## Slide 4: Impact of Receiver diversity techniques
Before SDM techniques were developed, receiver diversity was seen as a powerful communication receiver technique that provided wireless link improvement at relatively low cost.
Diversity techniques try to solve the problem that transmission errors occur when the transmission channel attenuation is large, i.e., when the channel is in a deep fade.

## Slide 5: Frequency and Time diversity
Frequency diversity is a technique that improves the performance of wireless systems by transmitting the same signal on multiple frequencies. The receiver then selects the frequency that has suffered least from fading or combines the signals from all frequencies to improve the estimation of the transmitted signal.
Time diversity transmits the same signal multiple times, with a time spacing between transmissions that is greater than the coherence time of the channel. This ensures that the multiple repetitions of the signal will be received with independent fading conditions.

## Slide 6: Space diversity
Space diversity, also known as antenna diversity, is a technique that improves the performance of wireless systems by using multiple antennas. The antennas are separated by a distance of half a radio wavelength or more, which ensures that the signals received by the antennas are uncorrelated. This means that if one antenna receives a weak signal, another antenna is likely to receive a strong signal.

## Slide 7: Polarization diversity
In wireless communication, polarization diversity is used to enhance reliability. It involves transmitting the same signal on two antennas with different polarizations, exploiting uncorrelated paths and combining horizontally and vertically polarized signals at the receiver for improved quality. This provides two diversity branches, simplifies antenna placement, but mixing with other diversity methods may degrade performance. The choice of diversity technique depends on the specific communication environment and system requirements.

## Slide 8: Selection diversity
Selection Diversity The highest instantaneous SNR branch is connected to the demodulator.

## Slide 9: Maximal Ratio and Equal Gain Combining
Maximal Ratio combining : Maximum Ratio Combining (MRC) is an optimization technique for combining signals that are carrying the same information.
Equal Gain combining : An Equal Gain Combiner is obtained when the gains used in MRC are all set to unity. The disadvantage is that (like MRC) an individual receiver for each antenna element is needed. However, the possibility of producing an acceptable signal from a number of unacceptable inputs is still retained, and the performance is only marginally inferior to MRC and usually superior to selection diversity.

## Slide 10: Multi-Antenna Link: Signal model and SDM techniques
One way to increase the capacity of wireless communication systems is by exploiting the spatial dimension using multiple antennas at the receiver as well as at the transmitter. This type of transmission is called Space Division Multiplexing (SDM).
In this chapter, a number of different decoding algorithms for SDM will be discussed and their performance will be compared.

## Slide 11: Signal model
We consider a communication system comprising Nt transmit (TX) and Nr receive (RX) antennas that operates in a Rayleigh flat-fading environment and exploits the spatial dimension by using Space Division Multiplexing (SDM).
A channel is said to be a Rayleigh fading channel when the channel impulse response is modelled as a zero-mean complex-valued gaussian process .
In this case, the envelope of the channel impulse response at any time instant has a Rayleigh probability distribution and the phase is uniformly distributed in the interval (0,2p).
This can be shown as follows. Suppose we model the channel impulse response H as a zero-mean complex gaussian variable, like:
H = A + jB

## Slide 12: Signal model
Where A and B are zero-mean statistically independent real guassian variables, each having a variance s2/2. The variance of the complex gaussian variable H can be shown to be:
var(H ) = E[H 2 ]- E[H ]2 = E[(A + jB)(A + jB)] = E[A2 + 2 jAB + B 2 ]= E[A2 ]+ E[B 2 ]= s 2
We introduce a new variable
Y = A2 + B 2
Here Y is chi-squared Random variable

## Slide 13: Signal model
Hence, the probability density function (pdf) of Y is:
pY (y) = e - y / 2 , y 0
Now, suppose we define a random variable R to denote the envelope of the channel impulse response:
R = =
In order to find the pdf of R, we need to make a change of variables in the Probability Distribution Function
(PDF) of Y to first find the PDF of R:
FR(r) = P(R ≤ r) = P(Y ≤ r) = P( ≤ r²) = F(r²)

## Slide 14: Signal model
where the fact is used that r ³ 0. Then the pdf of R is given by
pR® = FR(r) = Fy(r2) = 2 r pY(r2) = e – r 2 / 2 , r 0
This is the pdf of a Rayleigh-distributed random variable; thus, the envelope of H has a Rayleigh probability distribution. The fact that the phase of H is uniformly distributed in the interval (0,2p) .
Suppose that at discrete times, the transmitter sends an Nt-dimensional (complex) signal vector s (i.e., it transmits Nt parallel streams of data), and the receiver records an Nr-dimensional complex vector x. Then the following signal model describes the relation between s and x:
x = Hs + ν
where H is an Nr ´ Nt complex propagation matrix ) and the vector ν (Nr- dimensional) represents additive receiver noise

## Slide 15: Signal model
The vector s is assumed to have zero-mean, uncorrelated random variables with variance equal to ss2. The vector s is assumed to have zero-mean, uncorrelated random variables with variance equal to ss2. The total power of s (i.e., E[s*s]) is assumed to be P. Thus, the covariance matrix of s equals:
E[s*s] = ss2 INt = INt
Where * denotes the conjugate transpose of a vector or matrix and the matrix I with subscript Nt represents the identity matrix with dimension Nt
The channel matrix is denoted by H. It is assumed the channel matrix H has independently and identically distributed (i.i.d.), zero-mean, complex Gaussian, unit variance entries (the variance of each entry is sc2 = 1). In other words, each component has a Rayleigh distribution (like H) with s2 = sc2 = 1. Thus, the system operates in a Rayleigh flat-fading environment.

## Slide 16: Signal model
The vector ν is Nr-dimensional and represents additive receiver noise. The vector ν is assumed to have zero-mean, uncorrelated random variables with variance sn2 and a covariance matrix equal to:
E[v*v] = sv2 INt
Furthermore, it is assumed that the vectors s and ν are independent and thus the following holds: E[sν* ] = 0 . With the above-described assumptions about the power of the signal and the noise, the expected Signal-to- Noise Ratio (SNR) per receiving antenna, i.e., the SNR for each component of x, can be found and is equal to
= = =
Where Es stands for the signal power per receive antenna and N0 denotes the noise power per receive antenna.

## Slide 17: Signal model
In order to explain the different Space Division Multiplexing techniques, the following notations will be used
where xi and si represent the i-th element of x and s respectively. Hi and hi denote the i-th row and i-th column of H, respectively.
In the following sections, a number of SDM decoding techniques for the receiver will be discussed and compared.

## Slide 18: The Zero Forcing Algorithm
Zero Forcing algorithm is based on a conventional adaptive antenna array (AAA) technique.
Known as linear combinatorial nulling.
Each sub stream is considered to be the desired signal.
The remaining data streams are considered as "interferers“.
Nulling of the "interferers" can be performed by choosing weight vectors di (with i =1,2, ..., Nt) such that
Where T stands for transpose of a matrix.
And stands for jth column of the channel matrix H.

## Slide 19: The Zero Forcing Algorithm
Solving the weight vectors is equal to finding a matrix D such that :
D * H = I
Where D is a matrix that represents the linear processing in the receiver.
Forcing the ‘’interference’’ to zero , S is estimated.
If H is not square, then D equals the pseudo-inverse of H:
D = H+ = (H*H)-1 H*
Where + represent the pseudoinverse.
Some constraint for Pseudo-inverse
  Nt Nr
  The column of H must be independent

## Slide 20: The Zero Forcing Algorithm
If the inverse is the exists, the estimates of s can be found by:
  S est = Dx
  = (H*H)-1 H* x
  Or equivalently:
  S est = H+ x
And for i-th S est can be written as :
(S est) i = Hi+ x
Hi+ represent the I th row of H+ , is equal to the transpose of the i-th weight vector di
di is the so-called nulling vector.

## Slide 21: The Zero Forcing Algorithm
The ZF algorithm's performance can be tested through simulations, and its behavior can be theoretically understood by comparing it with the MRC system.
Understanding the diversity order helps relate the ZF algorithm to the MRC system.
This comparison gives valuable insights into the ZF algorithm's performance, making it crucial for evaluating wireless systems.

## Slide 22: Theoretical BER
In a system operating under Raleigh flat-fading, the channel elements can be expressed for an MRC system with one transmit and L receive antennas
The channel characteristics in the MRC system are determined by the channel elements , channel attenuation factor , and phase shift , assuming perfect channel knowledge.
The system output in a Raleigh flat-fading environment is represented by a single decision variable U for BPSK with Lth-order diversity:
        U = Re(xk) = Re( s + vk)
        Where vk denotes the complex gaussian noise and s is the transmitted symbol.
For BSPK, The decision variable U is used in the decoder to recover the transmitted s.
If U> 0 then s = and U < 0 then s = -

## Slide 23: Theoretical BER
For a fixed set of {} and the assumption that s = is transmitted.
The Gaussian decision variable U, with mean noise power N0 per receive antenna, determines the probability of being less than zero is :
P2 (b) = Q() where Q is the function as : Q(x) = dt and x
The SNR per bit , b is given as :
b = =
is the instantaneous SNR on the k-th channel. Because b can be seen as a chi-square
Distributed random variable with 2L degrees of freedom ,The pdf P(b) is :
P(b) =
Here is the average SNR per channel .

## Slide 24: Theoretical BER
To obtain BER, we need to average the conditional error probability:
P2 = P (b) d
Ther is closed-form solution for this integral, which can be expressed as :
P2 = [(1 - ) ]L[ (1 + ) ]K where
The conditional error probability is applicable for s = - and this leads to a total error probability of P2 /2 + P2 /2 = P2 ,when satisfy the condition >>1, the term (1 + )/2 1 and the term (1- ) , Furthermore,
=
Therefore , when is sufficiently large : P2

## Slide 25
Thank You for Cooperation Any Questions?