## Slide 1: Detection Error Probability Maximization for Disguised Full-Duplex Covert Communications
REFAT KHAN
Advised by Professor Jihwan Moon
Cognitive Communication System Lab
Department Of Mobile Convergence Engineering
Hanbat National University
May 27, 2024

## Slide 2: Outline
Biography
Abstract
.

## Slide 3: Biography
Education
Experience
Year | Degree | Major / Minor
2017-2021 | B.Eng., University of Information Technology and Sceience | Computer Science and Engineering
2022-2024 | M.Sc., Hanbat national Univeristy | Mobile convergence Engineering
Year | Organization | Position
2022.04 – 2022.06 | Nazdaq IT | Network Engineer
2020. 01 – 2022. 03 | Sp Wave | Junior Web developer

## Slide 4: Abstract
Research Focus:
  Reliable covert communications with disguised FD node.
  FD node: Appears half-duplex receive-only, transmits covertly.
Challenges:
  Detection by a warden node.
Methodology:
  Studied detection error probability (DEP).
  Derived optimal transmit power for FD node.
Key Findings:
  Optimal transmit power maximizes worst-case DEP.
  Ensures reliability of covert rate.
Results:
  Numerical validation of proposed solution.
  Impact of system parameters on DEP.
Conclusion:
  Guidance for secure communication design. Future research directions.

## Slide 5: System Model
2.1 Received Signals
  At the disguised FD destination
    Channel capacity for the public message
    Adaptive transmission policy with rate assumed, based on the feedback from the destination
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Source, S
Disguised FD destination, D
Covert Message,
Public Message,

## Slide 6: System Model
2.1 Received signals
  At the hidden receiver
    Channel capacity for the public message by treating the covert message as interference (if )
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Source, S
Public Message,
Covert Message,
Disguised FD destination, D
Hidden
receiver, R

## Slide 7: System Model
2.1 Received signals
  At the hidden receiver
    Achievable rate for the covert message after canceling the decoded public message
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Source, S
Public Message,
Covert Message,
Disguised FD destination, D
Hidden
receiver, R

## Slide 8: System Model
2.2 Covert Message Detection
  At the warden
    Achievable rate for the covert message after canceling the decoded public message
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Source, S
Public Message,
Covert Message,
Disguised FD destination, D
Warden, W

## Slide 9: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    The effective residual signal assuming the warden successfully decoded
    The null and alternative hypotheses
    The test statistics
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 10: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    Noise uncertainty
      Bounded uncertainty model with the mean noise power
      By change of variables with
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 11: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    Noise uncertainty
      Decision based on a threshold
      Detection error probability (DEP)
        False alarm probability
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 12: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    Noise uncertainty
      Decision based on a threshold
      Detection error probability (DEP)
      Miss probability
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 13: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    Noise uncertainty
      Decision based on a threshold
      Detection error probability (DEP)
        Assuming the equally probable chance of the covert message,
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 14: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    Noise uncertainty
      Decision based on a threshold
      Detection error probability (DEP)
        Assuming the equally probable chance of the covert message,
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 15: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    The shape of the DEP function
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Maximum error
= A random guess

## Slide 16: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    The shape of the DEP function
    Note that
    The first derivative
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 17: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    The shape of the DEP function
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Maximum error
= A random guess

## Slide 18: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    The minimum DEP and the optimal threshold
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 19: Problem Formulation
Covert rate maximization
  Objective function
    Minimum DEP
  Constraint 1
    Successive interference cancellation guaranteed
  Constraint 2
    Successful public message transmission guaranteed
  Constraint 3
    Minimum public rate threshold
  Constraint 4
    Minimum covet rate threshold
  Constraint 5
    To avoid zero DEP
  Constraint 6
    Power budget
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 20: Proposed Solution
Covert rate maximization
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Subject to :
Therefore, this leads to the optimal as

## Slide 21: Numerical Result
DEP vs. Source transmit power,
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Figure illustrates how the worst-case DEP changes with the source transmit power To ensure successful covert communication, it is necessary for the destination transmit power to be significantly lower than .

## Slide 22: Numerical Result
DEP vs. Minimum covert rate threshold,
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Figure presents a comparison of the average worst-case DEP with changes in the covert rate threshold . It's evident that the worst-case DEP exhibits a monotonically decreasing trend as the guaranteed covet rate increases.

## Slide 23: Numerical Result
DEP vs. Minimum quality of service for public message,
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Figure illustrates the average worst-case DEP for different minimum quality of services for public message . The average worst-case DEP decline in monotonic manner as increases.

## Slide 24: Numerical Result
DEP vs. Destination transmit power budget,
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Figure illustrates the average worst-case DEP​ for different the destination transmits power budget ​.Close performance among the presented schemes for low since the optimal is dominantly limited by .

## Slide 25: Conclusion
Covert communication setup
  Source node -> disguised full-duplex destination node
  Destination secretly transmit to the hidden receiver
Key Findings
  Optimal Transmit Power:
    Strong Destination-Receiver Link: Power tends towards zero
    Self-Interference: Poor suppression leads to near-zero power
    High Channel Gain to Warden: Power approaches zero
Insights:
  Low transmit power avoids detection
  Balance between covert communication and quality of service
Future Research:
  Explore practical modulation techniques
  Study the impact of imperfect CSI
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 26: Case 2: No channel information of eavesdroppers
② Closed-form solution by worst-case approximation
  Worst-case assumption where noise power is negligibly small at the eavesdroppers
    Conservative assumption
    An upper bound of the actual
  Properties of the upper bound
    increasing with
    Minimum at
Intro. Outline System Model Case I Case II Ext. Results Concl.

## Slide 27: Extension
Multi-user system (Chapter 2)
  Goal
    Secrecy performance maximization by jointly optimizing both the time allocation between the ET phase and the IT phases and the power allocation of the jammer for
Intro. Outline System Model Case I Case II Ext. Results Concl.
ET phase
The n-th IT phase
Jammer
H-AP
Eavesdroppers
Jammer
H-AP
User n
…
: Energy signal
: Information signal
: Jamming signal
…
…
Eavesdroppers
User n
…
…
…

## Slide 28: Numerical Results
  Compared schemes
    Equal resource allocation (ERA)
    Information rate maximization (IRM)
    Secure transmission without jammer
Intro. Outline System Model Case I Case II Ext. Results Concl.
Case 2: Secrecy outage probability
Case 1: Secrecy rate
35 %
50 %
10 dB

## Slide 29: Conclusion of Part I
Conclusion
  Secrecy performance of wiretap WPCN with the aid of an EH jammer
  Two different cases
    Perfect channel state information
      The optimal time allocation method for secrecy rate maximization
    No channel state information
      Both the optimal and closed-form time allocation method for secrecy outage minimization
  Extension to multi-user scenarios
Future works
  Relay-aided WPCN
  Multiple jammers
Intro. Outline System Model Case I Case II Ext. Results Concl.

## Slide 30: Relay-assisted Proactive Eavesdropping with Cooperative Jamming
Part II

## Slide 31: Introduction
Wireless surveillance via proactive eavesdropping
  Passive eavesdropping
    A legitimate monitor only listening to the suspicious communications
    Effective only when the eavesdropping link capacity is greater than or equal to the data rate of the suspicious users
  Proactive eavesdropping [JXu:17a]
    Proactive control on the channel condition in favor of eavesdropping
Intro. Outline System Model Case I Case II Ext. Results Concl.
Suspicious signal
Jamming signal
Suspicious link
Eavesdropping link
Simultaneous jamming
Suspicious
transmitter
Suspicious
receiver
Legitimate monitor

## Slide 32: Introduction
Relay-assisted proactive eavesdropping
  Common assumptions in literature [JXu:17b, CZhong:17]
    Existence of a direct link between the monitor and the suspicious users
      Possibly infeasible in practice (e.g., covert surveillance operation from a far distance)
      → Intermediate relays required
  Two practical considerations for relays [TRiihonen:09]
Intro. Outline System Model Case I Case II Ext. Results Concl.
Suspicious
transmitter
Suspicious
receiver
Relay
Central
monitor
Suspicious
transmitter
Suspicious
receiver
Relay
Central
monitor
Suspicious signal
Delayed suspicious signal
Negligible relay processing delay [YZeng:16]
e.g.) delay ≪ a symbol time period
Non-negligible relay processing delay
e.g.) delay > a symbol time period
Concurrent
Interference

## Slide 33: Introduction
Proposed relay-assisted proactive eavesdropping with a cooperative jammer
  Goal
    Eavesdropping rate maximization by optimizing the power allocation of the relay and the jammer
Intro. Outline System Model Case I Case II Ext. Results Concl.
Suspicious
transmitter
Suspicious
receiver
Full-duplex Eavesdropping
relay
Central
monitor
Jammer
Suspicious signal
Forwarded signal
Jamming signal

## Slide 34: Outline of Part II
System model
Case 1: Negligible relay processing delay
  Eavesdropping rate maximization
Case 2: Non-negligible relay processing delay
  Eavesdropping rate maximization
Extension
  Multi-antenna multi-relay system
Numerical results
Conclusion
Intro. Outline System Model Case I Case II Ext. Results Concl.

## Slide 35: System Model
Case 1: Negligible relay processing delay
  Received signals
    At the eavesdropping relay
    where
Intro. Outline System Model Case I Case II Ext. Results Concl.
: Transmit signal at node X
: Channel coefficient from node X to node Y
: Residual self-interference at node X
: Transmit power at node X
: Amplification factor
: AWGN at node X with power
Notations
Suspicious
transmitter
Suspicious
receiver
Eavesdropping relay
Central monitor
Jammer
Cooperative jamming

## Slide 36: System Model
Case 1: Negligible relay processing delay
  Received signals
    At the central monitor
    At the suspicious receiver
Intro. Outline System Model Case I Case II Ext. Results Concl.
Suspicious
transmitter
Suspicious
receiver
Eavesdropping relay
Central monitor
Jammer
Relay-like signal to the receiver

## Slide 37: System Model
Case 2: Non-negligible relay processing delay
  Received signals
    At the eavesdropping relay
    where
Intro. Outline System Model Case I Case II Ext. Results Concl.
Suspicious
transmitter
Suspicious
receiver
Eavesdropping relay
Central monitor
Jammer
Cooperative jamming

## Slide 38: System Model
Case 2: Non-negligible relay processing delay
  Received signals
    At the central monitor
    At the suspicious receiver
Intro. Outline System Model Case I Case II Ext. Results Concl.
Suspicious
transmitter
Suspicious
receiver
Eavesdropping relay
Central monitor
Jammer
Interference to the receiver

## Slide 39: Case 1: Negligible relay processing delay
Signal-to-interference-plus-noise ratio (SINR)
  and
  where
Problem formulation
  Optimal solution recovered by
Intro. Outline System Model Case I Case II Ext. Results Concl.
Problem 3. Eavesdropping rate maximization for case 1
Non-convex
Eavesdropping channel link
≥ Data rate of the suspicious users
Intercepting as much data as possible

## Slide 40: Case 1: Negligible relay processing delay
Properties of
  Constructive relay
    Maximum achievable when
  Destructive relay
    Minimum achievable when
Intro. Outline System Model Case I Case II Ext. Results Concl.
Suspicious
transmitter
Suspicious
receiver
Eavesdropping
relay

## Slide 41: Case 1: Negligible relay processing delay
Optimal solution for (P3)
Intro. Outline System Model Case I Case II Ext. Results Concl.
The optimal solution for (P3) falls into one of the following three modes:
1) Destructive relaying with full jamming: and
2) Constructive relaying with jamming: and
3) Constructive relaying without jamming: and
Theorem 2. Three operation modes
Mode 1
Mode 2
Mode 3
Closed-form
solutions available
Eavesdropping channel link
Data rate of the suspicious users

## Slide 42: Case 2: Non-negligible relay processing delay
Signal-to-interference-plus-noise ratio (SINR)
  and
  where
Problem formulation
Intro. Outline System Model Case I Case II Ext. Results Concl.
Problem 4. Eavesdropping rate maximization for case 2
Non-convex

## Slide 43: Case 2: Non-negligible relay processing delay
Two-step approach
  Step 1: Unconstrained solution by first relaxing the jammer power constraint
  Step 2: Retrieving the true optimal solution if the obtained jamming power from (P4.1) is
    Closed-form solution available
Intro. Outline System Model Case I Case II Ext. Results Concl.
Problem 4.1. Unconstrained problem for case 2
If , the optimal jamming power for the original problem (P4) is
Theorem 3. The optimal jamming power for the original problem (P4)
Solved by the two-layer algorithm (Part I.)

## Slide 44: Extension
Multi-antenna multi-relay system (Chapter 3 and 4)
  Goal
    Eavesdropping rate maximization by jointly optimizing the receive combining vector at the central monitor, the precoders at the relays and the transmit covariance matrix at the jammer
Intro. Outline System Model Case I Case II Ext. Results Concl.
Suspicious
transmitter
Suspicious
receiver
Eavesdropping
relay
Central
monitor
Jammer
Suspicious signal
Forwarded signal
Jamming signal
…
…

## Slide 45: Numerical Results
Intro. Outline System Model Case I Case II Ext. Results Concl.
Case 2: Non-negligible relay processing delay
Case 1: Negligible relay processing delay
68 %
Channel condition of the suspicious users
High
Low

## Slide 46: Conclusion of Part II
Conclusion
  A scenario where a distant central monitor covertly wiretaps the communication between a pair of suspicious users via a full-duplex relay and a cooperative jammer
  Two different cases
    Negligible relay processing delay
      Three optimal operation modes with the closed-form optimal solutions
    Non-negligible relay processing delay
      Two-step optimization approach for the optima power optimization
  Extension to multi-antenna multiple relay scenarios
Future works
  Absence of global channel state information
  Active suspicious users with anti-eavesdropping or anti-jamming capabilities
Intro. Outline System Model Case I Case II Ext. Results Concl.

## Slide 47: Reference
[RZhang:13] Rui Zhang and Chin Keong Ho, “MIMO broadcasting for simultaneous wireless information and power transfer,” IEEE Trans. Wireless Commun. vol. 12, pp. 1989-2001, May 2013.
[HJu:14] Hyungsik Ju and Rui Zhang, “Throughput maximization in wireless powered communication networks,” IEEE Trans. Wireless Commun. vol. 13, pp. 418-428, Jan. 2014.
[LLiu:14] Liang Liu, Rui Zhang and Kee-Chaing Chua, “Secrecy wireless information and power transfer with MISO beamforming,” IEEE Trans. Signal Process. vol. 64, pp. 1850-1863, Apr. 2014.
[DWKNg:14] Derrick Wing Kwan Ng, Ernest S. Lo and Robert Schober, “Robust beamforming for secure communication in systems with wireless information and power transfer,” IEEE Trans. Wireless Commun. vol. 13, pp. 4599-4615, Aug. 2014.
[HXing:16a] Hong Xing, Liang Liu and Rui Zhang, “Secrecy wireless information and power transfer in fading wiretap channel,” IEEE Trans. Veh. Technol. vol.65, pp. 180-190, Jan. 2016.
[WLiu:16] Wanchun Liu, Xiangyun Zhou, Salman Durrani and Petar Popovski, “Secure communication with a wireless-powered friendly jammer,” IEEE Trans. Wireless Commun. vol. 15, pp. 401-415, Jan. 2016.
[HXing:15b] Hong Xing and Kai-Kit Wong and Zheng Chu and Arumugam Nullanathan, ”To harvest and jam: a paradigm of self-sustaining friendly jammers for secure AF relaying,” IEEE Trans. Signal Process. vol. 63, pp. 6616-6631, Dec. 2015.
[JXu:17a] Jie Xu, Lingjie Duan and Rui Zhang, “Surveillance and intervention of infrastructure-free mobile communications: a new wireless security paradigm,” IEEE Wireless Commun. vol. 24, pp. 152-159, Aug. 2017.
[JXu:17b] Jie Xu, Lingjie Duan and Rui Zhang, “Proactive eavesdropping via cognitive jamming in fading channels,” IEEE Trans. Wireless Commun. vol. 16, pp. 2790-2806, May 2017.
[CZhong:17] Caijun Zhong, Xin Jiang, Fengzhong Qu and Zhaoyang Zhang, ”Multi-antenna wireless legitimate surveillance systems: design and performance analysis,” IEEE Trans. Wireless Commun. vol. 16, pp. 4585-4599, Jul. 2017.
[YZeng:16] Yong Zeng and Rui Zhang, “Wireless information surveillance via proactive eavesdropping with spoofing relay,” IEEE J. Sel. Topics Signal Process., vol. 10, pp. 1449-1461, Dec. 2016.

## Slide 48: Publications
Journal
    International journals
      1. Younghyun Jeon, Seok-Hwan Park, Changick Song, Jihwan Moon*, Seungjoo Maeng and Inkyu Lee, "Joint designs of fronthaul compression and precoding for full-duplex cloud radio access networks,“ IEEE Wireless Communications Letters, Vol. 5, No. 6, pp. 632 - 635, Dec. 2016.
      2. Jihwan Moon*, Hoon Lee, Changick Song and Inkyu Lee, "Secrecy performance optimization for wireless powered communication networks with an energy harvesting jammer,“ IEEE Transactions on Communications, Vol. 65, No. 2, pp. 764 - 774, Feb. 2017.
      3. Hoon Lee, Changick Song, Jihwan Moon* and Inkyu Lee, "Precoder designs for MIMO gaussian multiple access wiretap channels,“ IEEE Transactions on Vehicular Technology, Vol. 66, No. 9, pp. 8563 - 8568, Sept. 2017.
      4. Hanjin Kim, Hoon Lee, Seokju Jang, Jihwan Moon* and Inkyu Lee, "Maximization of minimum rate for wireless powered communication networks in interference channel,“ IEEE Communications Letters, Vol. 22, No. 8, pp. 1648 - 1651, Aug. 2018.
      5. Jihwan Moon*, Hoon Lee, Changick Song, Sunho Lee and Inkyu Lee, "Proactive eavesdropping with full-duplex relay and cooperative jamming,“ IEEE Transactions on Wireless Communications, Vol 17, No. 10, pp. 6707 - 6719, Oct. 2018.
      6. Jihwan Moon*, Hoon Lee, Changick Song, Seowoo Kang and Inkyu Lee, "Relay-assisted proactive eavesdropping with cooperative and spoofing,“ IEEE Transactions on Wireless Communications, Vol. 17, No. 10, pp. 6958 - 6971 Oct. 2018.
      7. Jihwan Moon*, Sanghyun Lee, Hoon Lee and Inkyu Lee, “Proactive eavesdropping with jamming and eavesdropping mode selection,“ submitted to IEEE Transactions on Wireless Communications.

## Slide 49: Publications
Conference
    International conference
      1. Jihwan Moon*, Hoon Lee, Changick Song and Inkyu Lee, "Secrecy outage minimization for wireless powered communication networks with an energy harvesting jammer,“ 2016 IEEE Global Communications Conference (GLOBECOM), Washington, DC, USA, 4 - 8 Dec. 2016.
      2. Jihwan Moon* and Inkyu Lee, "Secrecy performance of wireless powered communication network,“ The 32nd International Technical Conference on Circuits, Systems, Computers, and Communications (ITC-CSCC), Busan, Korea, 2 - 5 Jul. 2017.
      3. Jihwan Moon*, Hoon Lee, Changick Song and Inkyu Lee, "Multiple amplify-and-forward full-duplex relays for legitimate eavesdropping,“ 2018 IEEE International Conference on Communications (ICC), Kansas City, MO, USA, 20 - 24 May 2018.
      4. Jihwan Moon*, Hoon Lee, Changick Song and Inkyu Lee, "Time allocation methods for secure wireless powered communication networks,“ 2018 IEEE 88th Vehicular Technology Conference (VTC Fall), Chicago, IL, USA, 27 – 30 Aug. 2018.
      5. Jihwan Moon*, Hoon Lee, Changick Song, Seowoo Kang, Minseok Kim and Inkyu Lee, “Full-duplex spoofing relays for wireless surveillance,“ submitted to 2019 IEEE International Conference on Communications (ICC).
      6. Jihwan Moon*, Sanghyun Lee, Hoon Lee, Seunghwan Baek and Inkyu Lee, “Deep learning-based proactive eavesdropping for wireless surveillance,“ submitted to 2019 IEEE International Conference on Communications (ICC).
    Domestic conference
      1. Younghyun Jeon, Seok-Hwan Park, Changick Song, Jihwan Moon*, Seungjoo Maeng and Inkyu Lee, "Fronthaul designs with self-interference mitigation for full-duplex cloud radio access networks,“ 2017 Winter Conference of Korea Information and Communications Society, 18 - 20 Jan. 2017.
      2. Hanjin Kim, Hoon Lee, Seokju Jang, Jihwan Moon*, Junhee Park and Inkyu Lee, "Maximization of minimum rate for wireless powered communication networks in interference channel,“ 2018 Winter Conference of Korea Information and Communications Society, 17 - 19 Jan. 2018.