## Slide 1: Detection Error Probability Maximization for Disguised Full-Duplex Covert Communications
Refat Khan
Advised by Professor Jihwan Moon
Cognitive Communication System Lab
Department of Mobile Convergence Engineering
Hanbat National University
June 12, 2024

## Slide 2: Motivations
Securing Wireless Communication
  Wireless technology
    Transforms lives, but cyberattacks pose a threat, leading to potential information leaks
    To cope with this, cryptography has widely been adopted
  The perspective of physical layer security
    Yet, cryptography has limitations: complex key, IoT eavesdropping
    To examine the possibility of utilizing physical layer security
An approach of secure communications: Covert Communication
  Covert communication
    Opponents can conduct traffic analysis by collecting metadata during transmission.
    Vulnerabilities include capturing source and destination addresses, request-response frequency, etc.
Motivations Contributions
Alice
Bob
Eve

## Slide 3: Motivations
An approach of secure communications: Covert Communication
  Need for Covert Communications
    Combining cryptography and physical layer security can prevent eavesdropping
    Covert communications are necessary to counter traffic analysis threats
    Transmit data in a manner that avoids detection or suspicion
Unveiling Covert Communication: Discovering Full-Duplex (FD) Systems
  Full-Duplex (FD) Systems
    Enable real-time bidirectional communication
  Half-Duplex Systems
    Cause delays, reduce efficiency
  Advantage of FD in Covert Operations
    Transmit covertly, appear as receiver, enhances stealth
Motivations Contributions

## Slide 4: Contributions
Dissertation
  Detection Error Probability Maximization for Disguised Full-Duplex Covert Communications
Enhancing Covert Communication System Performance
  Overview
    Our research enhances the covert communication performance
  Covert Transmission
    Covert transmissions to hidden receiver via an unseen antenna
  Surveillance
    Monitored by warden node for suspicious communication
  Objectives
    Optimization of public data rate and transmit power of FD destination node to maximize DEP
    Prioritizing a minimum covert rate within the system
Motivations Contributions

## Slide 5: Outline
System model
Problem Formulation
Proposed Solution
Numerical results
Conclusion
.

## Slide 6: System Model
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Covert Message
Hidden Receiver, R
Source, S
Warden, W
Public Message
2. Schematic Diagram
Disguised FD destination, D
Self-interference

## Slide 7: System Model
2.1 Received signals
  At the disguised FD destination
    : Public message
    : Covert message
    : Transmit power at the source
    : Transmit power at the covert FD destination
    : Residual self interference after self interference cancellation
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Source, S
Public Message,
Covert Message,
Disguised FD destination, D

## Slide 8: System Model
2.1 Received Signals
  At the disguised FD destination
    Channel capacity for the public message
    Adaptive transmission policy with rate assumed, based on the feedback from the destination
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Source, S
Disguised FD destination, D
Covert Message,
Public Message,

## Slide 9: System Model
2.1 Received signals
  At the hidden receiver
    Channel capacity for the public message by treating the covert message as interference (if )
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Source, S
Public Message,
Covert Message,
Disguised FD destination, D
Hidden
receiver, R

## Slide 10: System Model
2.1 Received signals
  At the hidden receiver
    Achievable rate for the covert message after canceling the decoded public message
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Source, S
Public Message,
Covert Message,
Disguised FD destination, D
Hidden
receiver, R

## Slide 11: System Model
2.2 Covert Message Detection
  At the warden
    Achievable rate for the covert message after canceling the decoded public message
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Source, S
Public Message,
Covert Message,
Disguised FD destination, D
Warden, W

## Slide 12: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    The effective residual signal assuming the warden successfully decoded
    The null and alternative hypotheses
    The test statistics
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 13: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    Noise uncertainty
      Bounded uncertainty model with the mean noise power
      By change of variables with
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 14: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    Noise uncertainty
      Decision based on a threshold
      Detection error probability (DEP)
        False alarm probability
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 15: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    Noise uncertainty
      Decision based on a threshold
      Detection error probability (DEP)
      Miss probability
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 16: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    Noise uncertainty
      Decision based on a threshold
      Detection error probability (DEP)
        Assuming the equally probable chance of the covert message,
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 17: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    Noise uncertainty
      Decision based on a threshold
      Detection error probability (DEP)
        Assuming the equally probable chance of the covert message,
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 18: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    The shape of the DEP function
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Maximum error
= A random guess

## Slide 19: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    The shape of the DEP function
    Note that
    The first derivative
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 20: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    The shape of the DEP function
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Maximum error
= A random guess

## Slide 21: System Model
2.2 Covert Message Detection
  The worst-case assumption: known at the detector [HTa:20]
    The minimum DEP and the optimal threshold
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 22: Problem Formulation
Covert rate maximization
  Objective function
    Minimum DEP
  Constraint 1
    Successive interference cancellation guaranteed
  Constraint 2
    Successful public message transmission guaranteed
  Constraint 3
    Minimum public rate threshold
  Constraint 4
    Minimum covet rate threshold
  Constraint 5
    To avoid zero DEP
  Constraint 6
    Power budget
System Model Problem Formulation Proposed Solution Numerical Result Conclusion

## Slide 23: Proposed Solution
Covert rate maximization
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Subject to :
Therefore, this leads to the optimal as

## Slide 24: Numerical Result
System Parameter
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Parameter | Value
Bandwidth, 𝑊 | 20 [MHz]
𝑂-𝐗 Distance, , ∀𝐗∈{𝑆,𝐷,𝑅,𝑊} | 100 [m]
Source transmit power, | 23 [dBm]
Destination power budget, | 23 [dBm]
Minimum public data rate QoS, | 0.1 [bps/Hz]
Mean noise power at 𝑊, | - 160 [dBm/Hz]
Uncertainty bound around , | 5 [dB]
Noise power at and , , | - 160 [dBm/Hz]
Residual self-interference, | - 100 [dB]
Minimum covert data rate QoS, | 0.05 [bps/Hz]
Pathloss exponent | 3.5
Parameter | Value
Bandwidth, 𝑊 | 20 [MHz]
 | 100 [m]
 | 23 [dBm]
 | 23 [dBm]
 | 0.1 [bps/Hz]
 | - 160 [dBm/Hz]
 | 5 [dB]
 | - 160 [dBm/Hz]
 | - 100 [dB]
 | 0.05 [bps/Hz]
Pathloss exponent | 3.5

## Slide 25: Numerical Result
DEP vs. Source transmit power,
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
The destination transmit power must be significantly lower than to ensure covertness.
Higher increases worst-case DEP when is low, while lower is preferred when is high.

## Slide 26: Numerical Result
DEP vs. Minimum covert rate threshold,
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
Higher requires higher ,decreasing DEP.
"5% " and random schemes perform comparatively better than any other scheme.

## Slide 27: Numerical Result
DEP vs. Destination transmit power budget,
System Model Problem Formulation Proposed Solution Numerical Result Conclusion
When is low, both the "5% " and random schemes demonstrate performance close to the optimal scheme.
This closeness in performance arises because the influence of is dominant in this range by .

## Slide 28: Conclusion
Covert communication setup
  Source node disguised full-duplex destination node
  Destination secretly transmit to the hidden receiver
Key Findings
  Optimal Transmit Power:
    Strong Destination-Receiver Link: Power tends towards zero
    Self-Interference: Poor suppression leads to near-zero power
    High Channel Gain to Warden: Power approaches zero
Insights:
  Low transmit power avoids detection
  Balance between covert communication and quality of service
Future Research:
  Explore practical modulation techniques
  Study the impact of imperfect CSI
System Model Problem Formulation Proposed Solution Numerical Result Conclusion