## Slide 1: Disguised Full-Duplex Covert Communication *Jihwan Moon
2024.02.13
Presented by
Refat Khan
Department of Mobile Convergence Engineering, Hanbat National University

## Slide 2: Table of Contents
Introduction
System Model
Problem Formulation
Proposed Solution
Numerical Results
Discussion
Conclusion

## Slide 3: Introduction
Securing Wireless Communication:
Wireless technology transforms lives, but cyberattacks pose a threat, leading to potential information leaks.
To cope with this, cryptography has widely been adopted.
Yet, it has limitations: complex key generation and susceptibility to powerful eavesdroppers, especially challenging for IoT devices.
These downsides have led researchers to examine the possibility of utilizing physical layer security.
Its key feature is the ability to block wireless links to eavesdroppers using techniques like nullifying beamforming or introducing artificial noise.

## Slide 4: Introduction
Challenges of Secure Communication:
Security Threats:
  Opponents can conduct traffic analysis by collecting metadata during transmission.
  Vulnerabilities include capturing source and destination addresses, request-response frequency, etc
Need for Covert Communications:
  Transmit data in a manner that avoids detection or suspicion.
  Combining cryptography and physical layer security can prevent eavesdropping, but covert communications are necessary to counter traffic analysis threats.

## Slide 5: Introduction
Investigating Covert Communications:
System Overview:
  Setup involves a source node and disguised full-duplex (FD) destination node.
Objective:
  Ensure covert transmission to a hidden node while warden node surveillance.
Research Scope:
  Explore channel uncertainty at the warden node.
  Determine the lower bound of the expected minimum detection error probability (DEP).
Research Outcomes:
  Numerical results demonstrating covert rate performance under diverse DEP requirements
  Emphasis on the significance of secure and covert communication strategies against advanced security threats.

## Slide 6: System Model
Figure. System Model

## Slide 7: System Model
Covert Communication System Overview:
Communication Setup:
  Source node (S) transmitting a public message to the destination node (D)
  Covert transmission conducted by the seemingly receive-only destination node
  Covert signal transmitted to the hidden receiver (R) using an unseen antenna
Transmission Environment:
  Full-duplex (FD) communication implemented, allowing simultaneous transmission and reception
  Warden node (W) monitoring for suspicious communications
Key Focus:
  Ensuring secure and undetectable transmission from the destination to the hidden node
  Under surveillance of a warden node

## Slide 8: System Model
Received Signal in Covert Communication:
The received signal at the disguised full-duplex (FD) destination can be expressed as
Signal Information :
  Where hXY stands for the channel coefficient between node X and Y for X, Y ∈ {S, D, R, W},
  'Transmit power' at the destination indicated PD as and at the source as PS
  xP ∼ CN(0, 1) and xC ∼ CN(0, 1) denote the public and covert messages
Noise and Interference:
  'Residual self-interference channel' represented by CN(0, ) , accounting for residual signal interference
  ZX CN(0, ) 'Additive noise' at node X, reflecting the presence of additional background noise.

## Slide 9: System Model
CSI information:
The destination node can keep the CSI of the source node hSD since the covert transmission occurs internally under the normal S-D communications.
The hidden receiver can also easily estimate the CSI of the source and destination nodes.
If pilot sequences are informed from the destination node in advance during channel estimation.
Availability of CSI on the warden node, we assume the worst-case covert communications scenario in this work,
Meaning that the warden has the perfect knowledge of the CSI from the destination and hidden receiver to identify the worst-case achievable covert rate as a performance guideline in practice

## Slide 10: System Model
We know the Shannon capacity formula
So, the achievable public data rate
=
Hidden receiver receives both public and covert message
yR = hSR + + zR
It is required that the public data rate be limited by its achievable amount:
r̅PR =
Covert rate(rCR) after removing 𝑥𝑃 from 𝑦R
rCR =

## Slide 11: System Model
Covert Message Detection:
We then have the following two hypotheses:
Where the null hypothesis assumes there does not exist a covert message.
And the alternative hypothesis presumes that the source node did not send a covert message.
This work consider a radiometer as a detection means at the warden
The sufficient test statistic for after observing number of signals reduces to the average residual power
H0 : T =
𝐻1: 𝑇 = |ℎ𝐷𝑊|²𝑃𝐷 + 𝜎𝑊²

## Slide 12: System Model
Covert Message Detection:
The warden node decides that a covert transmission exists when and otherwise when with some threshold
We consider the uncertainty in the noise variance at the warden node.
Concretely, 𝜎𝑊,dB² ~ 𝑈(𝜎̅𝑊,dB² − dB, 𝜎̅𝑊,dB² + dB) in decibel scale with 𝜎̅𝑊,dB² and set to the mean and bounded range , respectively.
We then derive the DEP that consists of the false alarm and miss probabilities as
The warden node conjectures that the covert transmission randomly takes place with
Making use of the cumulative distribution function (CDF) of

## Slide 13: System Model
Covert Message Detection:
From Appendix A,
where
The PDF of becomes
The CDF of is obtained by
F

## Slide 14: System Model
The false alarm and miss probability are specifically written by
.
For

## Slide 15: System Model
For
We have two different cases depending on the value of and
For
When

## Slide 16: System Model
When

## Slide 17: System Model
When
For this case we can write

## Slide 18: System Model
 |  | 0 |  | 
0
1/2
Pr(error)
Maximum error =Random guess
A rough curve of Pr(error)

## Slide 19: System Model
Now the first derivative of with respect to
The first derivative is always positive indicating that function is always increasing.

## Slide 20: System Model
For
 |  | 0 |  | 
0
½
Maximum error
= Random
guess
Pr(error)

## Slide 21: System Model
The minimum DEP and optimal threshold

## Slide 22: System Model

## Slide 23: System Model
This is always positive for
therefore , the optimal threshold for the warden node in both above equation is determined by the boundary between and or and as
.

## Slide 24
Covert Message Detection:
. In contrast , if,
With , and
.
The warden node may desire a particular that can minimize the DEP.
Moreover, the first derivative of is calculated as
.
Covert Message Detection:
This is always positive for therefore , the optimal threshold for the warden node in both and is determined by the boundary between and or and as
.

## Slide 25: System Model
Note that Provides the worst-case minimum DEP assuming that the warden node knows the exact value of PD.
Problem Formulation:
In this work, we aim to identify the optimal public data rate and transmit power of the FD destination node that maximizes the covert rate at the hidden receiver as
…………………(17a)
Subject to : …………………(17b)
, …………………(17c)
, …………………(17d)
…………………(17e)
,
Constraint (17b) guarantees that the hidden receiver successfully decodes and eliminates a public message prior to decoding a covert message
(17c) indicates the achievable public data rate up to which the destination node can notify the source node to adjust.
A minimum quality of service for the public transmission is considered in (17d), and (17e) with (17f) assures the non-zero minimum DEP for .
Lastly, (17g) shows the power budget at the disguised FD destination node
Proposed Solution:
We first note that the covert rate in (17a) is an increasing function of PD while the upper limits of in (17b) and (17c) are decreasing functions of PD.
This means that the covert rate cannot exceed a value at which one of the upper limits becomes i.e ,)
Therefore, it is optimal for to be as low as possible for the maximum covert rate as

## Slide 26: System Model
Proposed Solution
We now simplify (P1) using the monotonicity of logarithms as
Subject to :

## Slide 27: System Model
The right-hand side of (19d) is larger than or equal to that of (19e) for , implying that satisfying (19d) automatically fulfills (19e).
Therefore, the optimal transmit power can be obtained by taking the minimum of the upper bounds from (19b)–(19d) and (19f) as
,

## Slide 28: Numerical results
Figure2. Node Placement

## Slide 29: Numerical results
Figure3. The average covert rat

## Slide 30: Numerical result
Figure 4. The average covert rate rCR versus the destination node power budget

## Slide 31: Numerical Results
Figure5.The average covert rate rCR versus the noise uncertainty bound

## Slide 32: Numerical Results
Figure6.The average covert rate rCR versus the minimum DEP threshold

## Slide 33: Numerical Results
Figure7. The average DEP versus the minimum DEP threshold

## Slide 34: Discussion
Performance:
Figures 3–7 show how adjusting transmit power at the destination influences covert rate performance.
Figure 3 highlights a connection between low source power and higher covert rates with more destination power, and vice versa.
Figure 7 indicates the importance of optimizing destination power for the best covert rate and minimum DEP threshold trade-off.

## Slide 35: Conclusion
Covert Communication System:
  Source node communicates with a disguised FD destination node.
  Destination node covertly sends critical messages to a hidden receiver, avoiding warden surveillance.
Optimization Goals:
  Studied optimal public data rate and transmit power for FD destination node.
  Objective: Maximize covert rate at the hidden receiver.
Closed-Form Solution Insights:
  Optimal destination transmit power trends:
    Approaches zero with an extremely strong destination–receiver link.
    Approaches zero if self-interference isn't sufficiently suppressed.
    Approaches zero with exceptionally high destination–warden channel gain

## Slide 36: Conclusion
Numerical Results:
  Phenomenon observed: Higher covert rate with more destination power when source power is low (and vice versa).
  Optimal destination power achieves the best balance between covert rate and minimum DEP threshold.
Practical Considerations:
  Work provides performance insights from an information-theoretic perspective.
  Future research suggestions: Explore practical modulations and imperfect CSI.

## Slide 37
Thank you for your Listening. For any queries, please email me at: refatkhanuits@gmail.com

## Slide 38: Conclusion
Quality CSI is indispensable for minimizing the Detection Error Probability (DEP) at the AF relay.
Accurate CSI facilitates optimal signal processing, enhancing the reliability and effectiveness of covert communication strategies.
High-quality CSI ensures robust covert communication, strengthening the security and efficiency of the system.